## Slide 1: http://www.comp.nus.edu.sg/~cs2100/
Lecture #13
Boolean Algebra

## Slide 2: Slido Link
You can ask questions here:
https://app.sli.do/event/4fVqZQwmoM7yUV24bQvuhp
Or scan this QR code. May be obstructed in some slides.

## Slide 3: Lecture #13: Boolean Algebra
Digital Circuits
Boolean Algebra
Truth Table
Precedence of Operators
Laws of Boolean Algebra
Duality
Theorems
Boolean Functions
Complement Functions
Standard Forms
Minterms and Maxterms
Canonical Forms: Sum-of-Minterms and Product-of-Maxterms

## Slide 4: 1. Digital Circuits (1/2)
Two voltage levels
  High/true/1/asserted
  Low/false/0/deasserted
Signals in digital circuit
High
Low
Signals in analog circuit
Advantages of digital circuits over analog circuits
  More reliable (simpler circuits, less noise-prone )
  Specified accuracy (determinable)
  Abstraction can be applied using simple mathematical model – Boolean Algebra
  Ease design, analysis and simplification of digital circuit – Digital Logic Design

## Slide 5: 1. Digital Circuits (2/2)
Combinational: no memory, output depends solely on the input
  Gates
  Decoders, multiplexers
  Adders, multipliers
Sequential: with memory, output depends on both input and current state
  Counters, registers
  Memories

## Slide 6: 2. Boolean Algebra
Truth tables
A | B | A  B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | B | A + B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | A'
0 | 1
1 | 0
Logic gates
A
B
AB
A
B
A+B
A
A'
Boolean values:
  True (T or 1)
  False (F or 0)
Connectives
  Conjunction (AND)
    A  B; A  B
  Disjunction (OR)
    A + B; A  B
  Negation (NOT)
    A'; ; ;
In CS2100, we use the symbols 1 for true, 0 for false, ∙ for AND, + for OR, and ' for negation (you may use the accent bar). Please follow.

## Slide 7: 2. Boolean Algebra: AND
Do write the AND operator ∙ (instead of omitting it)
  Example: Write a∙b instead of ab
  Why? Writing ab could mean that it is a 2-bit value.

## Slide 8: 3. Truth Table
Provide a listing of every possible combination of inputs and its corresponding outputs.
  Inputs are usually listed in binary sequence.
Example
  Truth table with 3 inputs x, y, z and 2 outputs (y + z) and (x  (y + z)).
x | y | z | y + z | x  (y + z)
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1

## Slide 9: 3. Proof using Truth Table
Prove: x  (y + z) = (x  y) + (x  z)
  Construct truth table for LHS and RHS
  Check that column for LHS = column for RHS
x | y | z | y + z | x  (y + z) | x  y | x  z | (x  y) + (x  z)
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

DLD page 59 Quick Review Questions Question 3-1.

## Slide 10: 4. Precedence of Operators
Precedence from highest to lowest
  Not (')
  And ()
  Or (+)
Examples:
  A  B + C = (A  B) + C
  X + Y' = X + (Y')
  P + Q'  R = P + ((Q')  R)
Use parenthesis to overwrite precedence. Examples:
  A  (B + C) [ Without parenthesis, it means AB+C or (AB)+C ]
  (P + Q)'  R [ Without parenthesis, it means P+Q'R or P+(Q'R) ]
Note the difference with CS1231/CS1231S. Here in CS2100, AND has higher precedence than OR.
Hence, A  B + C is not ambiguous in CS2100.

## Slide 11: 5. Laws of Boolean Algebra
Identity laws | 
A + 0 = 0 + A = A | A  1 = 1  A = A
Inverse/complement laws | 
A + A' = A' + A = 1 | A  A' = A'  A = 0
Commutative laws | 
A + B = B + A | A  B = B  A
Associative laws * | 
A + (B + C) = (A + B) + C | A  (B  C) = (A  B)  C
Distributive laws | 
A  (B + C) = (A  B) + (A  C) | A + (B  C) = (A + B)  (A + C)
* Due to the associative laws, A + B + C is unambiguous. It may be evaluated as A + (B + C) or (A + B) + C. Likewise for ABC.

## Slide 12: 6. Duality
If the AND/OR operators and identity elements 0/1 in a Boolean equation are interchanged, it remains valid.
Example:
  The dual equation of a+(bc)=(a+b)(a+c) is a(b+c)=(ab)+(ac).
Duality gives free theorems – “two for the price of one”, as a Boolean equation is logically equivalent to its dual. So, you prove one theorem and the other comes for free!
Examples:
  If (x+y+z)' = x'y'z' is valid, then its dual (xyz)' = x'+y'+z' is also valid.
  If x+1 = 1 is valid, then its dual x0 = 0 is also valid.
Do not confuse duality with negation!

## Slide 13: 7. Theorems
Idempotency | 
X + X = X | X  X = X
One element / Zero element | 
X + 1 = 1 + X = 1 | X  0 = 0  X = 0
Involution | 
( X' )' = X | 
Absorption 1 | 
X + XY = X | X(X + Y) = X
Absorption 2 | 
X + X'Y = X + Y | X(X' + Y) = XY
DeMorgans’ (can be generalised to more than 2 variables) | 
(X + Y)' = X'  Y' | (X  Y)' = X' + Y'
Consensus | 
XY + X'Z + YZ = XY + X'Z | (X+Y)(X'+Z)(Y+Z) = (X+Y)(X'+Z)

## Slide 14: 7. Proving a Theorem
Theorems can be proved using truth table, or by algebraic manipulation using other theorems/laws.
Example: Prove absorption theorem X + XY = X
  X + XY = X1 + XY (by identity law)
  = X(1+Y) (by distributivity)
  = X1 (by one element law) = X (by identity law)
By the principle of duality, we may also cite (without proof) that X(X+Y) = X.

## Slide 15: 8. Boolean Functions
Examples of Boolean functions (logic equations):
  F1(x,y,z) = xyz'
  F2(x,y,z) = x + y'z
  F3(x,y,z) = x'y'z + x'yz + xy'
  F4(x,y,z) = xy' + x'z
x | y | z | F1 | F2 | F3 | F4
0 | 0 | 0 | 0 |  |  | 
0 | 0 | 1 | 0 |  |  | 
0 | 1 | 0 | 0 |  |  | 
0 | 1 | 1 | 0 |  |  | 
1 | 0 | 0 | 0 |  |  | 
1 | 0 | 1 | 0 |  |  | 
1 | 1 | 0 | 1 |  |  | 
1 | 1 | 1 | 0 |  |  | 
From the truth table, F3 = F4.
Can you prove F3 = F4 by using Boolean Algebra?
x | y | z | F1 | F2 | F3 | F4
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 0 | 0
1 | 1 | 1 | 0 | 1 | 0 | 0


## Slide 16: 9. Complement Functions

Given a Boolean function F, the complement of F, denoted as F', is obtained by interchanging 1 with 0 in the function’s output values.
Example: F1 = xyz'
What is F1' ?
  F1' = (xyz')' = x' + y' + (z')' (DeMorgan’s) = x' + y' + z (Involution)
x | y | z | F1 | F1'
0 | 0 | 0 | 0 | 
0 | 0 | 1 | 0 | 
0 | 1 | 0 | 0 | 
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | 0 | 
x | y | z | F1 | F1'
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 1

## Slide 17: 10. Standard Forms (1/2)
Certain types of Boolean expressions lead to circuits that are desirable from an implementation viewpoint.
Two standard forms:
  Sum-of-Products (SOP)
  Product-of-Sums (POS)
Literals
  A Boolean variable on its own or in its complemented form
  Examples: (1) x, (2) x', (3) y, (4) y'
Product term
  A single literal or a logical product (AND) of several literals
  Examples: (1) x, (2) xyz', (3) A'B, (4) AB, (5) dg'vw

## Slide 18: 10. Standard Forms (2/2)
Sum term
  A single literal or a logical sum (OR) of several literals
  Examples: (1) x, (2) x+y+z', (3) A'+B, (4) A+B, (5) c+d+h'+j
Sum-of-Products (SOP) expression
  A product term or a logical sum (OR) of several product terms
  Examples: (1) x, (2) x + yz', (3) xy' + x'yz, (4) AB + A'B', (5) A + B'C + AC' + CD
Product-of-Sums (POS) expression
  A sum term or a logical product (AND) of several sum terms
  Examples: (1) x, (2) x(y+z'), (3) (x+y')(x'+y+z), (4) (A+B)(A'+B'), (5) (A+B+C)D'(B'+D+E')
Every Boolean expression can be expressed in SOP or POS form.
DLD page 59 Quick Review Questions Questions 3-2 to 3-5.

## Slide 19: Quiz Time!

Put the right ticks in the following table.
 | Expression | SOP? | POS?
(1) | X'∙Y + X∙Y' + X∙Y∙Z |  | 
(2) | (X+Y')∙(X'+Y)∙(X'+Z') |  | 
(3) | X' + Y + Z |  | 
(4) | X∙(W' + Y∙Z) |  | 
(5) | X∙Y∙Z' |  | 
(6) | W∙X'∙Y + V∙(X∙Z + W') |  | 












SOP expr: A product term or a logical sum (OR) of several product terms.
POS expr: A sum term or a logical product (AND) of several sum terms.

## Slide 20: 11. Minterms and Maxterms (1/2)
A minterm of n variables is a product term that contains n literals from all the variables.
  Example: On 2 variables x and y, the minterms are:
  x'∙y', x'∙y, x∙y' and x∙y
A maxterm of n variables is a sum term that contains n literals from all the variables.
  Example: On 2 variables x and y, the maxterms are:
  x'+y', x'+y, x+y' and x+y
In general, with n variables we have up to 2n minterms and 2n maxterms.

## Slide 21: 11. Minterms and Maxterms (2/2)
The minterms and maxterms on 2 variables are denoted by m0 to m3 and M0 to M3 respectively.
Important fact: Each minterm is the complement of its corresponding maxterm. Likwise, each maxterm is the complement of its corresponding minterm.
  Example: m2 = x∙y' m2' = ( x∙y' )' = x' + ( y' )' = x' + y = M2
x | y | Minterms |  | Maxterms | 
 |  | Term | Notation | Term | Notation
0 | 0 | x'∙y' | m0 | x+y | M0
0 | 1 | x'∙y | m1 | x+y' | M1
1 | 0 | x∙y' | m2 | x'+y | M2
1 | 1 | x∙y | m3 | x'+y' | M3

## Slide 22
Ability to convert minterms and maxterms from its Boolean expression to its notation (and vice versa) is important.
Test yourself with the following quiz, assuming that you are given a Boolean function on 4 variables A, B, C, D.
 | Boolean expression | Minterm notation
(1) | A'∙B'∙C∙D | m3
(2) |  | m10
(3) |  | m11
(4) | A∙B∙C∙D' | 
(5) | A∙B'∙C'∙D | 
Quiz Time Again!
Minterm
 | Boolean expression | Maxterm notation
(1) | A+B+C'+D' | M3
(2) |  | M13
(3) |  | M0
(4) | A+B+C'+D | 
(5) | A'+B+C+D' | 
Maxterm
A∙B'∙C∙D'
A∙B'∙C∙D
m14
m9
A'+B'+C+D'
A+B+C+D
M2
M9

## Slide 23: 12. Canonical Forms
Canonical/normal form: a unique form of representation.
  Sum-of-minterms = Canonical sum-of-products
  Product-of-maxterms = Canonical product-of-sums

## Slide 24: 12.1 Sum-of-Minterms
Given a truth table, example:
x | y | z | F1 | F2 | F3
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 1 | 0
1 | 1 | 1 | 0 | 1 | 0
Obtain sum-of-minterms expression by gathering the minterms of the function (where output is 1).
F3 = x'∙y'∙z + x'∙y∙z + x∙y'∙z' + x∙y'∙z = m1 + m3 + m4 + m5 = Sm(1,3,4,5) or Sm(1,3 – 5)
F1 = x∙y∙z' = m6
F2 = x'∙y'∙z + x∙y'∙z' + x∙y'∙z + x∙y∙z' + x∙y∙z = m1 + m4 + m5 + m6 + m7 = Sm(1,4,5,6,7) or Sm(1,4 – 7)


## Slide 25: 12.2 Product-of-Maxterms

Given a truth table, example:
x | y | z | F1 | F2 | F3
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 1 | 0
1 | 1 | 1 | 0 | 1 | 0
Obtain product-of-maxterms expression by gathering the maxterms of the function (where output is 0).
F3 = (x+y+z) ∙ (x+y'+z) ∙ (x'+y'+z) ∙ (x'+y'+z') = M0 ∙ M2 ∙ M6 ∙ M7 = PM(0,2,6,7)
F2 = (x+y+z) ∙ (x+y'+z) ∙ (x+y'+z') = M0 ∙ M2 ∙ M3 = PM(0,2,3)

## Slide 26: 12.3 Conversion of Standard Forms
We can convert between sum-of-minterms and product-of-maxterms easily
Example: F2 = Sm(1,4,5,6,7) = PM(0,2,3)
Why? See F2' in truth table.
x | y | z | F2 | F2'
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0
F2' = m0 + m2 + m3 Therefore, F2 = (m0 + m2 + m3)' = m0' ∙ m2' ∙ m3' (by DeMorgan’s) = M0 ∙ M2 ∙ M3 (as mx' = Mx)
  Read up DLD section 3.4, pg 57 – 58.
  Quick Review Questions: pg 60 – 61, Q3-6 to 3-13.

## Slide 27: End of File