## Slide 1: http://www.comp.nus.edu.sg/~cs2100/
Recitation 8
Combinational Circuits
18 March 2024
Aaron Tan

## Slide 2: Contents
K-maps (quick review)
Design Methods
    Gate-level design method
    Block-level design method
Magnitude Comparator
Circuit Delays
Quizzes

## Slide 3: K-maps
K-maps – get simplified SOP (sum-of-products) expression.
Step 1: Find all PIs (biggest groupings of 1s).
Step 2: Find EPIs among the PIs.
EPIs must appear in answer.
Find minimum number of (non-essential) PIs to cover the 1s not covered by the EPIs.
EPI: A PI that contains at least one minterm that is not covered by any other PI.
Finding simplified POS (product-of-sums) expression for F.
Step 1: Draw K-map of F’.
Step 2: Find simplified SOP expression for F’
Step 3: Invert both sides – get simplified POS expression for F.
K-maps with don’t cares – A PI must have at least one minterm in it.

## Slide 4: K-maps (Tutorial 6 D3)
0
0
0
0
0
1
0
0
1
1
0
1
1
0
0
1
C
D
A
B
(a) F1(A,B,C,D) = m(5, 8, 10, 12, 13, 14)
PI:
EPI:
3
2
Simplified SOP expr:
F1 =
AD’ + BC’D

## Slide 5: K-maps (Tutorial 6 D3)
0
0
1
0
1
1
1
1
1
1
1
1
0
0
1
0
Y
Z
W
X
(b) F2(W,X,Y,Z) = M(0, 1, 2, 8, 9, 10)
PI:
EPI:
2
2
Simplified SOP expr:
F2 =
X + YZ

## Slide 6: K-maps (Tutorial 6 D3)
X
1
0
0
0
X
1
0
0
1
X
1
X
0
0
1
M
N
K
L
(c) F3(K,L,M,N) = m(1, 7, 10, 13, 14) + d(0, 5, 8, 15)
PI:
EPI:
6
1
Simplified SOP expr:
F3 =
LN
+ KMN’ + K’L’M’
LN
+ KMN’ + K’M’N

## Slide 7: K-maps (Tutorial 6 D3)
1
1
X
X
0
1
X
X
0
1
1
X
0
0
0
X
C
D
A
B
(d) F4(A,B,C,D) = M(4, 8, 9, 11, 12)  D(2, 3, 6, 7, 10, 14)
PI:
EPI:
4
2
Simplified SOP expr:
F4 =
BD + A’B’

## Slide 8: summary
Design Methods

## Slide 9: QUICK REVIEW
K-Maps

## Slide 10: 1. Introduction
Two classes of logic circuits
  Combinational
  Sequential
Combinational Circuit
  Each output depends entirely on the immediate (present) inputs.
Combinational
Logic
: :
inputs
outputs
: :
Sequential Circuit
  Each output depends on both present inputs and state.
Memory
Combinational
Logic
: :
inputs
outputs
: :

## Slide 11: 3. Design Methods
Different combinational circuit design methods:
  Gate-level design method (with logic gates)
  Block-level design method (with functional blocks)
Design methods make use of logic gates and useful function blocks
  These are available as Integrated Circuit (IC) chips.
  Types of IC chips (based on packing density): SSI, MSI, LSI, VLSI, ULSI.
Main objectives of circuit design:
  Reduce cost (number of gates for small circuits; number of IC packages for complex circuits)
  Increase speed
  Design simplicity (re-use blocks where possible)

## Slide 12: 4. Gate-Level (SSI) Design: Half Adder (1/2)
Design procedure:
  1. State problem Example: Build a Half Adder.
  2. Determine and label the inputs and outputs of circuit. Example: Two inputs and two outputs labelled, as shown below.
  3. Draw the truth table.
X | Y | C | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
X
Y
S
C
(X + Y)
Half
Adder


## Slide 13: 4. Gate-Level (SSI) Design: Half Adder (2/2)
  4. Obtain simplified Boolean functions. Example: C = XY S = X'Y + XY' = XY
  5. Draw the logic diagram.
X | Y | C | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
X
Y
S
C
Half Adder
X
Y
S
C
(X + Y)
Half
Adder

Block diagram of Half Adder

## Slide 14: 4. Gate-Level (SSI) Design: Full Adder (1/5)
Half adder adds up only two bits.
To add two binary numbers, we need to add 3 bits (including the carry).
  Example:
Need Full Adder (so called as it can be made from two half adders).
X
Y
Z
S
C
(X + Y + Z)
Full
Adder


## Slide 15: 4. Gate-Level (SSI) Design: Full Adder (2/5)
Truth table:
Using K-map, simplified SOP form:
  C = XY + XZ + YZ S = X'Y'Z + X'YZ' + XY'Z' + XYZ
Note:
Z - carry in (to the current position)
C - carry out (to the next position)
X | Y | Z | C | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1

0
1
00 01 11 10
X
YZ
1
1
1
1
C
0
0
0
0
0
1
00 01 11 10
X
YZ
1
1
1
1
S
0
0
0
0

## Slide 16: 4. Gate-Level (SSI) Design: Full Adder (3/5)
Alternative formulae using algebraic manipulation:
  C = XY + XZ + YZ = XY + (X + Y)Z = XY + ( (XY) + XY )Z = XY + (XY)Z + XYZ = XY + (XY)Z
  S = X'Y'Z + X'YZ' + XY'Z' + XYZ = X'(Y'Z + YZ') + X(Y'Z' + YZ) = X'(YZ) + X(YZ)' = X(YZ)

## Slide 17: 4. Gate-Level (SSI) Design: Full Adder (4/5)
Circuit for above formulae:
  C = XY + (XY)Z
  S = X(YZ) = (XY)Z (XOR is associative)
Full Adder made from two Half-Adders (+ an OR gate).
(XY)
X
Y
S
C
Z
(XY)

## Slide 18: 4. Gate-Level (SSI) Design: Full Adder (5/5)
Circuit for above formulae:
  C = XY + (XY)Z
  S = X(YZ) = (XY)Z (XOR is associative)
Full Adder made from two Half-Adders (+ an OR gate).
(XY)
X
Y
S
C
Z
(XY)
Half
Adder
Half
Adder
X
Y
X
Y
Sum
Carry
Sum
Carry
Block diagrams

## Slide 19: 4. Gate-Level (SSI) Design: Code Converters
Code converter – takes an input code, translates to its equivalent output code.
Code
converter
Input
code
Output
code
Example: BCD to Excess-3 code converter.
  Input: BCD code
  Output: Excess-3 code

## Slide 20: 4. BCD to Excess-3 Code Converter (1/3)
Digit | BCD code | Excess-3 code
0 | 0000 | 0011
1 | 0001 | 0100
2 | 0010 | 0101
3 | 0011 | 0110
4 | 0100 | 0111
5 | 0101 | 1000
6 | 0110 | 1001
7 | 0111 | 1010
8 | 1000 | 1011
9 | 1001 | 1100

## Slide 21: 4. BCD to Excess-3 Code Converter (2/3)
Truth table:
 | BCD |  |  |  | Excess-3 |  |  | 
 | A | B | C | D | W | X | Y | Z
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
2 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1
3 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0
4 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1
5 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0
6 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
7 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 0
8 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1
9 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0
10 | 1 | 0 | 1 | 0 | X | X | X | X
11 | 1 | 0 | 1 | 1 | X | X | X | X
12 | 1 | 1 | 0 | 0 | X | X | X | X
13 | 1 | 1 | 0 | 1 | X | X | X | X
14 | 1 | 1 | 1 | 0 | X | X | X | X
15 | 1 | 1 | 1 | 1 | X | X | X | X
K-maps:
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
1
1
1
1
1
W
0
0
0
0
0
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
1
1
1
1
1
X
0
0
0
0
0
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
1
1
1
1
1
Y
0
0
0
0
0
1
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
1
1
1
1
Z
0
0
0
0
0

## Slide 22: 4. BCD to Excess-3 Code Converter (3/3)
1
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
1
1
1
1
Z
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
1
1
1
1
1
W
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
1
1
1
1
1
X
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
1
1
1
1
1
Y
W = A + BC + BD
X = B'C + B'D + BC'D'
Y = C.D + C'.D'
Z = D'


## Slide 23: 5. Block-Level Design
More complex circuits can also be built using block-level method.
In general, block-level design method (as opposed to gate-level design) relies on algorithms or formulae of the circuit, which are obtained by decomposing the main problem to sub-problems recursively (until small enough to be directly solved by blocks of circuits).
First example shows how to create a 4-bit parallel adder using block-level design.
Using 4-bit parallel adders as building blocks, we can create the following:
  1. BCD-to-Excess-3 Code Converter
  2. 16-bit Parallel Adder

## Slide 24: 5. 4-bit Parallel Adder (1/4)
Consider a circuit to add two 4-bit numbers together and a carry-in, to produce a 5-bit result.
4-bit
Parallel Adder
C5
C1
X2
X1
Y4
Y3
S4
S3
S2
S1
Y2
Y1
X4
X3
Black-box view of 4-bit parallel adder
5-bit result is sufficient because the largest result is: 11112 + 11112 + 12 = 111112

## Slide 25: 5. 4-bit Parallel Adder (2/4)
SSI design (gate-level design) technique should not be used here.
Truth table for 9 inputs is too big: 29 = 512 rows!
Simplification becomes too complicated!
X4X3X2X1 | Y4Y3Y2Y1 | C1 | C5 | S4S3S2S1
0 0 0 0 | 0 0 0 0 | 0 | 0 | 0 0 0 0
0 0 0 0 | 0 0 0 0 | 1 | 0 | 0 0 0 1
0 0 0 0 | 0 0 0 1 | 0 | 0 | 0 0 0 1
… | … | … | … | …
0 1 0 1 | 1 1 0 1 | 1 | 1 | 0 0 1 1
… | … | … | … | …
1 1 1 1 | 1 1 1 1 | 1 | 1 | 1 1 1 1

## Slide 26: 5. 4-bit Parallel Adder (3/4)
Alternative design possible.
Addition formula for each pair of bits (with carry in), Ci+1Si = Xi + Yi + Ci has the same function as a full adder: Ci+1 = Xi Yi + (Xi Yi)Ci Si = Xi  Yi  Ci
C =
X = 1 0 1 0
Y = 1 1 1 1
X + Y =
0
1
1
0
1
1
0
0
1

## Slide 27: 5. 4-bit Parallel Adder (4/4)
Cascading 4 full adders via their carries, we get:
C1
Y1 X1
S1
FA
C2
C5
Y2 X2
S2
FA
C3
Y3 X3
S3
FA
C4
Y4 X4
S4
FA
Output
Input
Note that carry is propagated by cascading the carry from one full adder to the next.
Called Parallel Adder because inputs are presented simultaneously (in parallel). Also called Ripple-Carry Adder.

## Slide 28: 5. 16-bit Parallel Adder
Larger parallel adders can be built from smaller ones.
Example: A 16-bit parallel adder can be constructed from four 4-bit parallel adders:
4-bit // adder
X4..X1
Y4..Y1
C1
S4..S1
4-bit // adder
X8..X5
Y8..Y5
C5
S8..S5
4-bit // adder
X12..X9
Y12..Y9
C9
S12..S9
4-bit // adder
X16..X13
Y16..Y13
C13
S16..S13
C17
4
4
4
4
4
4
4
4
4
4
4
4
A 16-bit parallel adder
4
S4..S1
S4S3S2S1
=

## Slide 29: 5. BCD to Excess-3 Converter: Revisit (1/2)
Excess-3 code can be converted from BCD code using truth table:
 | BCD |  |  |  | Excess-3 |  |  | 
 | A | B | C | D | W | X | Y | Z
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
2 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1
3 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0
4 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1
5 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0
6 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
7 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 0
8 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1
9 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0
10 | 1 | 0 | 1 | 0 | X | X | X | X
11 | 1 | 0 | 1 | 1 | X | X | X | X
12 | 1 | 1 | 0 | 0 | X | X | X | X
13 | 1 | 1 | 0 | 1 | X | X | X | X
14 | 1 | 1 | 1 | 0 | X | X | X | X
15 | 1 | 1 | 1 | 1 | X | X | X | X
Gate-level design can be used since only 4 inputs.
However, alternative design is possible.
Use problem-specific formula:
  Excess-3 code = BCD Code + 00112

## Slide 30: 5. BCD to Excess-3 Converter: Revisit (2/2)
Block-level circuit:
4-bit Parallel Adder
X4
X3
X2
X1
Y4
Y3
Y2
Y1
0
0
1
1
S4
S3
S2
S1
BCD
code
Excess-3
code
unused
0
Cin
Cout
A BCD to Excess-3 Code Converter
Note: In the lab, input 0 (low) is connected to GND, 1 (high) to Vcc.

## Slide 31: 7. Example: 6-Person Voting System
Application: 6-person voting system.
  Use FAs and a 4-bit parallel adder.
  Each FA can sum up to 3 votes.
Voter 1
3-bit Output
A
B
S
Cout
S
Cin
Voter 2
Voter 3
Voter 4
A
B
S
Cout
S
Cin
Voter 5
Voter 6
Full-adder 1
Full-adder 2
S
Cout
Cin
A
1
2
3
4
B
1
2
3
4
S
1
2
3
4
Parallel adder
1
0
1
0
1
0
0
1
1
0
1
1
0
1
1
0
1
1
1
0
1
1
1
1
0
1


## Slide 32: summary
Magnitude Comparator

## Slide 33: 8. Magnitude Comparator (1/4)
Magnitude comparator: compares 2 unsigned values A and B, to check if A>B, A=B, or A<B.
To design an n-bit magnitude comparator using classical method, it would require 22n rows in truth table!
We shall exploit regularity in our design.
Question: How do we compare two 4-bit unsigned values A (a3a2a1a0) and B (b3b2b1b0)?
  If (a3 > b3) then A > B
  If (a3 < b3) then A < B
  If (a3 = b3) then if (a2 > b2) …

## Slide 34: 8. Magnitude Comparator (2/4)
Let A = A3A2A1A0 , B = B3B2B1B0; xi = AiBi + Ai'Bi'
A2
B2
A3
B3
A0
B0
A1
B1
(A < B)
(A > B)
(A = B)
x3
x2
x1
x0
A3'B3
A3B3'
A3'B3 + x3A2'B2
+ x3x2.A1'B1
+ x3x2x1A0'B0
A3B3' + x3A2B2'
+ x3x2A1B1'
+ x3x2x1A0B0'
x3x2x1x0


## Slide 35: 8. Magnitude Comparator (3/4)
Block diagram of a 4-bit magnitude comparator
A3
A2
A1
A0
4-bit Comp
(A < B)
(A > B)
(A = B)
B3
B2
B1
B0
0
1
1
0
1
0
1
0
1
0
0
A3
A2
A1
A0
4-bit Comp
(A < B)
(A > B)
(A = B)
B3
B2
B1
B0
0
1
1
0
0
0
1
1
0
1
0

## Slide 36: 8. Magnitude Comparator (4/4)

A function F accepts a 4-bit binary value ABCD, and returns 1 if 3  ABCD  12, or 0 otherwise. How would you implement F using magnitude comparators and a suitable logic gate?
A3
A2
A1
A0
4-bit Comp
(A < B)
(A > B)
(A = B)
B3
B2
B1
B0
A3
A2
A1
A0
4-bit Comp
(A < B)
(A > B)
(A = B)
B3
B2
B1
B0
A3
A2
A1
A0
4-bit Comp
(A < B)
(A > B)
(A = B)
B3
B2
B1
B0
A3
A2
A1
A0
4-bit Comp
(A < B)
(A > B)
(A = B)
B3
B2
B1
B0
A
B
C
D
0
0
1
0
1
1
0
1
F

## Slide 37: summary
Circuit Delays

## Slide 38: 9. Circuit Delays (1/5)
Given a logic gate with delay t. If inputs are stable at times t1, t2, …, tn, then the earliest time in which the output will be stable is: max( t1, t2, …, tn ) + t
t1
Logic
Gate
t2
tn
:
:
max (t1, t2, ..., tn ) + t
To calculate the delays of all outputs of a combinational circuit, repeat above rule for all gates.

## Slide 39: 9. Circuit Delays (2/5)
As a simple example, consider the full adder circuit where all inputs are available at time 0. Assume each gate has delay t.
Outputs S and C experience delays of 2t and 3t respectively.
max(0,0)+t = t
t
X
Y
S
C
Z
0
0
0
max(t,0)+t = 2t
max(t,2t)+t = 3t
2t

## Slide 40: 9. Circuit Delays (3/5)
More complex example: 4-bit parallel adder.
C1
Y1 X1
S1
FA
C2
C5
Y2 X2
S2
FA
C3
Y3 X3
S3
FA
C4
Y4 X4
S4
FA
0
0
0
0
0
0
0
0
0

## Slide 41: 9. Circuit Delays (4/5)
Analyse the delay for the repeated block.
where Xi, Yi are stable at 0t, while Ci is assumed to be stable at mt.
Full
Adder
Xi
Yi
Ci
Si
Ci+1
0
0
mt
Performing the delay calculation:
Xi
Yi
Si
Ci+1
Ci
max(0,0)+t = t
t
0
0
mt
max(t,mt)+t
max(t,mt)+2t
max(t,mt)+t

## Slide 42: 9. Circuit Delays (5/5)
Calculating:
  When i=1, m=0; S1 = 2t and C2 = 3t
  When i=2, m=3; S2 = 4t and C3 = 5t
  When i=3, m=5; S3 = 6t and C4 = 7t
  When i=4, m=7; S4 = 8t and C5 = 9t
In general, an n-bit ripple-carry parallel adder will experience the following delay times:
  Sn = ( (n – 1)2 + 2 ) t
  Cn+1 = ( (n – 1)2 + 3 ) t
Propagation delay of ripple-carry parallel adders is proportional to the number of bits it handles.
Maximum delay: ( (n – 1)2 + 3 ) t
Full
Adder
Xi
Yi
Ci
Si
Ci+1
0
0
mt
max(t,mt)+t
max(t,mt)+2t

## Slide 43: quizzes
Lecture 17 Quiz 1
Lecture 17 Quiz 2

## Slide 44: Lecture 17 Quiz 1 Q1

## Slide 45: Lecture 17 Quiz 2 Q1
w=ab
x=b+c
c'
  F = w  x
  = w'x + wx'
  = (a.b)'(b+c) + (a.b)(b+c)'
  = (a'+b').(b+c) + (a.b).(b'.c')
  = a'.b + a'.c + b'.b + b'.c + a.b.b'.c'
  = a'.b + a'.c + 0 + b'.c + 0
  = a'.b + a'.c + b'.c
  = a'.b + b'.c
Concensus Theorem:
XY + X'Z + YZ = XY + X'Z

## Slide 46: Lecture 17 Quiz 2 Q2, Q3
1ns
2ns
2ns
3ns
2ns
5ns
4ns

## Slide 47: End of File