## Slide 1: Protocols

## Slide 2: Background

## Slide 3: Quality of Service (QoS)
Basic concepts
  Quality of Service (QoS)
  Quality of Experience (QoE)
  Resource reservation
End-to-end path must respond to real-time requirements and provide a certain level of service quality

## Slide 4: QoS vs QoE
QoS – Quality of Service:
  Network characteristics/behavior
  Performance guarantees given by network provider based on measurements
QoE – Quality of Experience:
  Impact of network behavior on end user
    some imperfections may go unnoticed
    some imperfections may render application useless
  Not captured by network measurements
    a 5% packet loss could be invisible if it affects background
    a missed target due to a 100ms delay can affect game outcome
© Magda El Zarki

## Slide 5: QoE/QoS Factors
Possible QoE/QoS factors:
  Startup delay
  Stall events
  Quality switches
  Visual quality measure:
    PSNR: Peak Signal-to-Noise Ratio
    SSIM, SSIMPlus Index: try to model human visual perception
Wang, Z., Bovik, A. C., Sheikh, H. R., and Simoncelli, E. P.,
“Image quality assessment: From error visibility to structural similarity,“
IEEE Trans. Image Processing 13, 600−612 (Apr. 2004).

## Slide 6: PSNR
Mean Square Error (MSE):
    M, N: Columns and rows, i.e., pixels
PSNR:
    R: input value domain range, e.g., 255

## Slide 7: Multimedia Systems
QoS, QoE
  Often “quality” is subjective (e.g., video, audio)
Real-time requirements
  Hard real-time: aircraft control system
  Soft real-time: e.g., video playback

## Slide 8: Real-time Requirements
Fault tolerance
Missed deadlines
  Result: e.g., jitter
Periodic sampling: streams
  Affects scheduling policy
Bandwidth demand
  Bandwidth versus quality tradeoff

## Slide 9: Service and Protocol Req.
Time-sensitive requirements
High data throughput requirements
Service guarantee requirements
High or partial reliability requirements
Cost-based fairness requirements

## Slide 10: Resource Reservation
Proper resource management helps to establish desired QoS/QoE (memory, bandwidth, CPU, …)
E.g.: network bandwidth
  Circuit-switched
  Packet-switched
versus

## Slide 11: Resource Reservation
Rule of Thumb
E.g.: In circuit-switched telephone system “silence” will consume bandwidth
Shared resources can often be more (cost-) effectively used compared with dedicated resources

## Slide 12: QoS Summary
(Networked) multimedia systems have certain requirements
Best-effort, shared network: Internet
Non real-time OS: Windows, Linux
But, we have
Need to find clever techniques

## Slide 13: You are Here
Network
Encoder
Sender
Middlebox
Receiver
Decoder

## Slide 14: Interested ISO Layers
Application
Transport
Network

## Slide 15: Interested ISO Layers
RTP, RTSP, HTTP
TCP
Network
IP Multicast
IP
UDP

## Slide 16: IP Multicast

## Slide 17: Communication Models
Traditional applications:
One-to-One
Receiver
Sender

## Slide 18: Communication Models
Media applications:
One-to-Many
Sender
Receivers

## Slide 19: Communication Models
Media applications:
Many-to-Many
Mesh topology

## Slide 20: Communication Models
Media applications:
Many-to-Many
Star topology
(client-server)
Example:
MCU for video conferencing
(Multipoint Control Unit)

## Slide 21: Traditional Solutions
Mesh
  N-1 connections at each client
  (N × (N-1))/2 connections total
  Not scalable!
Star
  1 connection per client
  Server resources become a bottleneck
  Single point of failure

## Slide 22: Example
YouTube: client-server video distribution
Throughput: > 6 billion hours watched each month (2014)
Number of users: >1 billion per month
Video codecs: (Sorenson H.263), H.264/MPEG-4 AVC, VP8, VP9
Container formats: MP4, WebM (DASH)
Video bit-rate: 200 to 5,900 kb/s (SD to 1080p HD to “4K” (3072p))
Cost of bandwidth: several million US$ per month, CDN for popular videos
Notes: http://archive.infoworld.com/articles/hn/xml/99/08/16/990816hnmentors.xml

## Slide 23: One Solution: IP Multicast
Sender
Receivers

## Slide 24: Group and Members
Members

## Slide 25: Sending to a Group

## Slide 26: Joining and Leaving

## Slide 27: Anyone can Send

## Slide 28: Multicast Address
Group ID or “Multicast address”
  224.0.0.0 – 239.255.255.255

## Slide 29: Unicast
Router
Router
Router
Router
A
B
C
S
A
B
C

## Slide 30: Multicast
Router
Router
Router
Router
A
B
C
S
G

## Slide 31: Multicast
Router
Router
Router
Router
A
B
C
S
G
G

## Slide 32: Multicast
Router
Router
Router
Router
A
B
C
S
G
G

## Slide 33: Question 1
Router
G
?
Should I forward this packet to my subnet?

## Slide 34: Group Management
Routers maintain “local host group membership table”
“Which group has a member in my subnet ?”
 IP Multicast requires ‘state’ in each router.

## Slide 35: Question 2
Router
Router
Router
Router
Which neighbors should I forward this packet?

## Slide 36: IP Multicast: Current State
IP multicast has been standardized long ago and is implemented in almost all major routers, but
Technical and non-technical reasons hinder its adoption in much of the Internet.
Can you think of some reasons?

## Slide 37: One/Many-to-Many (1)
Because of the unavailability of IP multicast many applications use application-level multicast.
 Push protocols (e.g., use of distribution trees): sender is pushing data to nodes/receivers.
 Pull protocols: receivers are pulling data from nodes/source.

## Slide 38: One/Many-to-Many (2)
Frequently also unicast is still used.
But, unicast creates scalability problems.
Possible solutions:
  CDN: Content Distribution Networks (e.g., Akamai)
  Caching.

## Slide 39: Routing Protocols
For push multicast

## Slide 40: Routing Protocols
Generic Methods :
  Form a tree to all routers with members
  Deliver the packets along the tree

## Slide 41: Shortest Path Tree
One tree for each source for each group

## Slide 42: Shared Tree
One tree for each group

## Slide 43: Routing Protocols
DVMRP – shortest path tree
CBT – shared tree
PIM – combine both

## Slide 44: DVMRP
Distance Vector Multicast Routing Protocol

## Slide 45: DVMRP
Used to share information between routers for the transportation of IP multicast packets.
RFC 1075.
Basis of Mbone.

## Slide 46: From S to G
R
P
Q
T
S
:

## Slide 47
R
P
Q
T
Is R on the shortest path to S ?
S
:

## Slide 48: If no…, ignore the packet
R
P
Q
T

## Slide 49: If yes…
R
P
Q
T
Where should I forward it to ?

## Slide 50
R
P
Q
T
Is my subnet
interested?

## Slide 51
R
P
Q
T
?
?
Are my
neighbors
interested?

## Slide 52: Observation
If neighbor is going to ignore my packets, don’t need to send the packets to it.

## Slide 53
R
P
Q
T
Exchanging Routing Tables
Dest | Next Hop | Cost
S | P | 4
A | T | 3
B | P | 2

## Slide 54: Flooding
Default : Always send to neighboring routers, unless told otherwise.

## Slide 55: Pruning
Routers which received a “useless” packet send a prune message back. “Don’t send me packets addressed to G anymore !”

## Slide 56
R
P
Q
T

## Slide 57
R
P
Q
T
PRUNE

## Slide 58
R
P
Q
T

## Slide 59
R
P
Q
T
GRAFT

## Slide 60
R
P
Q
T

## Slide 61
R
P
Q
T
PRUNE

## Slide 62: A router needs to remember …
If it has any member for group G in its subnet
Where to forward packets from source S to group G
  Which neighbors will not throw my packets away
  Which sub-trees are pruned

## Slide 63: Problems of DVMRP
Not Scalable
  O(|S||G|)
Not Efficient
  Flooding initially
  Periodically exchange routing tables

## Slide 64: CBT
Core-based Tree

## Slide 65: Core Based Tree
One tree per group
Pick a router as core

## Slide 66: A Shared Tree
core
P
Q
R
U
V
W

## Slide 67: V Joins G
core
P
Q
R
U
V
JOIN
W

## Slide 68: V Joins G
core
P
Q
R
U
V
JOIN
W

## Slide 69: V Joins G
core
P
Q
R
U
V
ACK
W

## Slide 70: V Joins G
core
P
Q
R
U
V
ACK
W

## Slide 71: V Joins G
core
P
Q
R
U
V
W

## Slide 72: U Joins G
core
P
Q
R
U
V
JOIN
W

## Slide 73: U Joins G
core
P
Q
R
U
V
ACK
W
intercept!

## Slide 74: P Sends (on Tree)
core
P
Q
R
U
V
W

## Slide 75: W Sends (Not on Tree)
core
P
Q
R
U
V
W

## Slide 76: CBT Strengths
Scalable
  O(|G|) states
No flooding
No exchange of states

## Slide 77: CBT Weaknesses
Core placement matters
Single point of failure
Core can become bottleneck
Paths not always shortest

## Slide 78: PIM
Protocol Independent Multicast

## Slide 79: PIM
Get the best of both worlds:
  dense mode : similar to DVMRP
  sparse mode : similar to CBT

## Slide 80: Summary
What is IP Multicast?
How to route packets
  IGMP
  DVMRP/CBT/PIM

## Slide 81: So, Why Can’t We Multicast?
Who assigns a multicast address?
Who pays for multicast traffic?
How to inter-operate between protocols?
How can we prevent DoS?

## Slide 82: Multicast Programming

## Slide 83: Create a UDP Socket
s = socket(PF_INET, SOCK_DGRAM, 0)
bind(s, sock_addr, sizeof(sock_addr))

## Slide 84: Join a Group
struct sockaddr_in groupStruct;
struct ip_mreq mreq;
mreq.imr_multiaddr = … // init mcast addr
setsockopt(s, IPPROTO_IP, IP_ADD_MEMBERSHIP, (char *) &mreq, sizeof(mreq))

## Slide 85: Leave a Group
struct sockaddr_in groupStruct;
struct ip_mreq mreq;
mreq.imr_multiaddr = … // init mcast addr
setsockopt(s, IPPROTO_IP, IP_DROP_MEMBERSHIP, (char *) &mreq, sizeof(mreq))

## Slide 86: Transport Layer

## Slide 87: Interested ISO Layers
RTP
TCP
Network
IP Multicast
IP
UDP

## Slide 88: TCP vs UDP

## Slide 89: TCP vs UDP
TCP
  connection oriented
  packet ordering
  reliability
  congestion control
UDP
  just send!

## Slide 90: How TCP Works (Roughly)
Sender expects packet to be ACK’ed
If received duplicate ACKs or no ACK after RTO, assume packet lost

## Slide 91: How TCP Works (Roughly)
Congestion Avoidance - Reduce sending window when packet lost, increase when packet gets through

## Slide 92: Conventional Wisdom
Continuous media uses UDP
  Retransmission may not be useful
  Congestion control makes throughput unpredictable
  Multicast + TCP has problems

## Slide 93: UDP Header
struct UDPHeader
{
short src_port;
short dst_port;
short length;
short checksum;
}

## Slide 94: UDP not enough
Who sent this packet?
How do I interpret this packet?
When was this packet generated?
Which packets come first?
Is this packet important?
Should I ask for retransmission?

## Slide 95: UDP Challenges
“NATmare” (© Nan Chen, Atrica)
  Many residential computers use network address translation (NAT)
Peer 1
Peer 2
NAT device
(Cable modem gateway)
NAT device
(DSL gateway)
192.168.0.1
192.168.1.3
128.125.4.204
209.7.114.157

## Slide 96: NAT Solutions
UDP Hole Punching
  Third party host is used to initially establish correct state in the routers
  State periodically expires: keep-alive message may be needed in the absence of traffic
  STUN protocol (RFC 5389) “Session Traversal Utilities for NAT”

## Slide 97: Application-Level Framing
Expose details to applications
Let application decide what to do with a packet, not transport protocol

## Slide 98: SIP
Session Initiation Protocol

## Slide 99: SIP
Application-layer control (signaling) protocol for creating, modifying, and terminating sessions with one or more participants.
Text-based
RFC 3261
Has been accepted as a standard for VoIP (Note: Skype does not use SIP)