## Slide 1: https://www.comp.nus.edu.sg/~cs2100/
CS2100
Recitation 11
Pipelining
6 April 2026
Aaron Tan

## Slide 2: Contents
MIPS Pipeline
Pipeline Hazards
QnA
Pipelining Quiz
Selected Past Years’ Exam Questions
  AY2020/21 Sem2 Q16
  AY2023/24 Sem1 Q16
Additional exercise
  Tracing signals and data in a pipeline

## Slide 3: MIPS Pipeline

## Slide 4: 2. MIPS Pipeline Stages
Five Execution Stages
  IF: Instruction Fetch
  ID: Instruction Decode and Register Read
  EX: Execute an operation or calculate an address
  MEM: Access an operand in data memory
  WB: Write back the result into a register
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
Program Flow
(Instructions)
Time
Several instructions are in the pipeline simultaneously!

## Slide 5: 3. MIPS Pipeline: Datapath
Single-cycle implementation:
  One cycle per instruction.
  Update all state elements (PC, register file, data memory) within a clock cycle.
Pipelined implementation:
  One cycle per pipeline stage.
  Data required for each stage needs to be stored separately (why?)
Data used by subsequent instructions:
  Store in programmer-visible state elements: PC, register file and memory
Data used by same instruction in later pipeline stages:
  Additional registers in datapath called pipeline registers
  IF/ID: register between IF and ID
  ID/EX: register between ID and EX
  EX/MEM: register between EX and MEM
  MEM/WB: register between MEM and WB

## Slide 6: 3. MIPS Pipeline: Datapath
Coloured rectangles are pipeline registers
Why no pipeline register at the end of WB stage?

## Slide 7: 3. Pipeline Datapath: IF Stage
At the end of a cycle, IF/ID receives (stores):
  Instruction read from InstructionMemory[PC]
  PC + 4
PC + 4
  Also connected to one of the MUX's inputs (another coming later)
ID Stage
At the beginning of a cycle IF/ID register supplies: | At the end of a cycle ID/EX receives:
Register numbers for reading two registers 16-bit offset to be sign-extended to 32-bit PC + 4 | Data values read from register file 32-bit immediate value PC + 4

## Slide 8: 3. Pipeline Datapath: EX Stage
MEM Stage
At the beginning of a cycle ID/EX register supplies: | At the end of a cycle EX/MEM receives:
Data values read from register file 32-bit immediate value PC + 4 | (PC + 4) + (Immediate x 4) ALU result isZero? signal Data Read 2 from register file
At the beginning of a cycle EX/MEM register supplies: | At the end of a cycle MEM/WB receives:
(PC + 4) + (Immediate x 4) ALU result isZero? signal Data Read 2 from register file | ALU result Memory read data

## Slide 9: 3. Pipeline Datapath: WB Stage
At the beginning of a cycle MEM/WB register supplies: | At the end of a cycle
ALU result Memory read data | Result is written back to register file (if applicable) There is a bug here…….
3. Corrected Datapath
The “Write register” number supplied by the IF/ID pipeline register is for another instruction!
Solution:
  Pass “Write register” number from ID/EX through EX/MEM to MEM/WB pipeline register for use in WB stage
  i.e. let the "Write register" number follows the instruction through the pipeline until it is needed in WB stage

## Slide 10: 3. Corrected Datapath

## Slide 11: 4. Pipeline Control: Main Idea
Same control signals as single-cycle datapath
Difference: Each control signal belongs to a particular pipeline stage

## Slide 12: 4. Pipeline Control: Grouping
Group control signals according to pipeline stage
 | RegDst | ALUSrc | MemToReg | Reg Write | Mem Read | Mem Write | Branch | ALUop | 
 |  |  |  |  |  |  |  | op1 | op0
R-type | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
lw | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
sw | X | 1 | X | 0 | 0 | 1 | 0 | 0 | 0
beq | X | 0 | X | 0 | 0 | 0 | 1 | 0 | 1
 | EX Stage |  |  |  | MEM Stage |  |  | WB Stage | 
 | RegDst | ALUSrc | ALUop |  | Mem Read | Mem Write | Branch | MemToReg | Reg Write
 |  |  | op1 | op0 |  |  |  |  | 
R-type | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1
lw | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 1
sw | X | 1 | 0 | 0 | 0 | 1 | 0 | X | 0
beq | X | 0 | 0 | 1 | 0 | 0 | 1 | X | 0

## Slide 13: 4. Pipeline Control: Implementation
Signal generated in ID stage
Signal used in EX stage and onwards
Signal propagated along until utilized

## Slide 14: 4. Pipeline Control: Datapath and Control

## Slide 15: Ideal Pipeline (i.e., No Hazards)
 |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | F | D | E | M | W |  |  |  |  |  | 
 | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
Instr-1 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Instr-2 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Instr-3 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Instr-4 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Instr-5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Instr-6 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Instr-7 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Instr-8 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Instr-9 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Instr-10 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Number of cycles required = 14 cycles
I = No. of instructions.
N = No. of pipeline stages.
No. of cycles = I + (N – 1).

## Slide 16: Pipeline Hazards

## Slide 17: Pipeline Hazards
3 types of pipeline hazards
  Structural hazards
  Data hazards
  Control hazards

## Slide 18: 2. Structural Hazard: Memory
Solution: Split memory into Data and Instruction memory
Mem
Instruction Order
Time (clock cycles)
Load
Inst1
Inst2
Inst3
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Reg
Mem
Reg
Load uses Data Memory
Inst3 uses Instr. Memory

## Slide 19: 2. Structural Hazard: Register File
Mem
Instruction Order
Inst0
Inst1
Inst2
Inst3
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Reg
Mem
Reg
Time (clock cycles)
Recall that registers are very fast memory.
Solution: Split cycle into half; first half for writing into a register; second half for reading from a register.
Inst0 writes into the register during the first half of the cycle.
Inst3 reads from the register during the second half of the cycle.

## Slide 20: 4. RAW Data Hazards
Value from prior instruction is needed before write back
C
C
1
C
C
2
C
C
3
C
C
4
C
C
5
C
C
6
T
i
m
e
(
i
n
c
l
o
c
k
c
y
c
l
e
s
)
C
C
7
C
C
8
C
C
9
1
0
1
0
1
0
1
0
1
0
/
–
2
0
–
2
0
–
2
0
–
2
0
–
2
0
V
a
l
u
e
o
f
r
e
g
i
s
t
e
r
$
2
:
I
M
R
e
g
I
M
R
e
g
s
u
b
$
2
,
$
1
,
$
3
a
n
d
$
1
2
,
$
2
,
$
5
I
M
R
e
g
D
M
R
e
g
I
M
D
M
R
e
g
I
M
D
M
R
e
g
o
r
$
1
3
,
$
6
,
$
2
a
d
d
$
1
4
,
$
2
,
$
2
s
w
$
1
5
,
1
0
0
(
$
2
)
D
M
R
e
g
R
e
g
R
e
g
R
e
g
D
M
Data
dependency
No problem

## Slide 21: Data Hazards: Forwarding technique (1/2)

## Slide 22: Data Hazards: Forwarding technique (2/2)
Forwarding removes all delay, except for lw (why?)
With forwarding, there is still 1 cycle of delay for the instruction after lw.

## Slide 23: 5. Control Dependency: Why?
Decision is made in MEM stage:
Too late!

## Slide 24: 5. Control Dependency: Example
R
e
g
R
e
g
C
C
1
T
i
m
e
(
i
n
c
l
o
c
k
c
y
c
l
e
s
)
4
0
b
e
q
$
1
,
$
3
,
7
P
r
o
g
r
a
m
e
x
e
c
u
t
i
o
n
o
r
d
e
r
(
i
n
i
n
s
t
r
u
c
t
i
o
n
s
)
I
M
R
e
g
I
M
D
M
I
M
D
M
I
M
D
M
D
M
D
M
R
e
g
R
e
g
R
e
g
R
e
g
R
e
g
R
e
g
I
M
4
4
a
n
d
$
1
2
,
$
2
,
$
5
4
8
o
r
$
1
3
,
$
6
,
$
2
5
2
a
d
d
$
1
4
,
$
2
,
$
2
7
2
l
w
$
4
,
5
0
(
$
7
)
C
C
2
C
C
3
C
C
4
C
C
5
C
C
6
C
C
7
C
C
8
C
C
9
R
e
g
Wrong
Execution!

## Slide 25: 6. Control Hazards: Stall Pipeline?
R
e
g
C
C
1
T
i
m
e
(
i
n
c
l
o
c
k
c
y
c
l
e
s
)
4
0
b
e
q
$
1
,
$
3
,
7
P
r
o
g
r
a
m
e
x
e
c
u
t
i
o
n
o
r
d
e
r
(
i
n
i
n
s
t
r
u
c
t
i
o
n
s
)
I
M
R
e
g
D
M
D
M
R
e
g
R
e
g
I
M
7
2
l
w
$
4
,
5
0
(
$
7
)
C
C
2
C
C
3
C
C
4
C
C
5
C
C
6
C
C
7
C
C
8
C
C
9
Bubble
Bubble
Bubble
Bubble
Bubble
Bubble
Bubble
Bubble
Bubble
Bubble
Bubble
Bubble
Bubble
Bubble
Bubble
Wait until the branch outcome is known and then fetch the correct instructions
 Introduces 3 clock cycles delay

## Slide 26: Control Hazards
Techniques to reduce stalls:
      Early Branching resolution
        Move branch decision calculation to earlier pipeline stage
      Branch Prediction
        Guess the outcome of the branch
      Delayed Branching
        Do something useful while waiting for the outcome

## Slide 27: Control Hazards: Early Branching
Branch resolution made at stage 2 (ID stage)
Sign
extend
ALU
result
ALU
ALUcontrol
4
Zero
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 1
Read
data 2
RegWrite
Instruction
Register File
16
32
To branch
Control logic
Add
Shift
left 2
PC + 4
Branch target
address calculation
Register Comparison
Target address
QnA:
Q2: Why can’t the next instruction be fetched right after the branch instruction’s ID stage in early branching? Isn’t the branch target address calculated in the EX stage?

## Slide 28: 6.1 Reduce Stalls: Early Branch (3/3)
R
e
g
C
C
1
T
i
m
e
(
i
n
c
l
o
c
k
c
y
c
l
e
s
)
4
0
b
e
q
$
1
,
$
3
,
7
P
r
o
g
r
a
m
e
x
e
c
u
t
i
o
n
o
r
d
e
r
(
i
n
i
n
s
t
r
u
c
t
i
o
n
s
)
I
M
R
e
g
D
M
D
M
R
e
g
R
e
g
I
M
7
2
l
w
$
4
,
5
0
(
$
7
)
C
C
2
C
C
3
C
C
4
C
C
5
C
C
6
C
C
7
C
C
8
C
C
9
Bubble
Bubble
Bubble
Bubble
Bubble
Wait until the branch decision is known:
  Then fetch the correct instruction
Reduced from 3 to 1 clock cycle delay

## Slide 29: 6.1 Early Branch: Problems (1/3)
However, if the register(s) involved in the comparison is produced by preceding instruction:
  Further stall is still needed!
R
e
g
I
M
R
e
g
I
M
C
C
1
C
C
2
C
C
3
C
C
4
C
C
5
C
C
6
T
i
m
e
(
i
n
c
l
o
c
k
c
y
c
l
e
s
)
P
r
o
g
r
a
m
e
x
e
c
u
t
i
o
n
o
r
d
e
r
(
i
n
i
n
s
t
r
u
c
t
i
o
n
s
)
I
M
R
e
g
D
M
R
e
g
C
C
7
C
C
8
C
C
9
D
M
R
e
g
R
e
g
D
M
add $s0, $s1, $s2
beq $s0, $s3, Exit
Bubble
$s0 is needed before it is produced!
You solved one problem, but introduced another problem!

## Slide 30: 6.1 Early Branch: Problems (2/3)
Solution:
  Add forwarding path from ALU to ID stage
  One clock cycle delay is still needed
R
e
g
I
M
R
e
g
I
M
C
C
1
C
C
2
C
C
3
C
C
4
C
C
5
C
C
6
T
i
m
e
(
i
n
c
l
o
c
k
c
y
c
l
e
s
)
P
r
o
g
r
a
m
e
x
e
c
u
t
i
o
n
o
r
d
e
r
(
i
n
i
n
s
t
r
u
c
t
i
o
n
s
)
I
M
R
e
g
D
M
R
e
g
C
C
7
C
C
8
C
C
9
D
M
R
e
g
R
e
g
D
M
add $s0, $s1, $s2
beq $s0, $s3, Exit
Bubble
Bubble

## Slide 31: 6.1 Early Branch: Problems (3/3)
Problem is worse with load followed by branch
Solution:
  MEM to ID forwarding and 2 more stall cycles!
  In this case, we ended up with 3 total stall cycles  no improvement!
R
e
g
I
M
R
e
g
I
M
C
C
1
C
C
2
C
C
3
C
C
4
C
C
5
C
C
6
T
i
m
e
(
i
n
c
l
o
c
k
c
y
c
l
e
s
)
P
r
o
g
r
a
m
e
x
e
c
u
t
i
o
n
o
r
d
e
r
(
i
n
i
n
s
t
r
u
c
t
i
o
n
s
)
I
M
R
e
g
D
M
R
e
g
C
C
7
C
C
8
C
C
9
D
M
R
e
g
R
e
g
D
M
lw $s0, 0($s1)
beq $s0, $s3, Exit
Bubble
Bubble
Bubble
ALU  ID forwarding cannot help!

## Slide 32: 6.2 Reduce Stalls: Branch Prediction
There are many branch prediction schemes
  We only cover the simplest in this course 
Simple prediction:
  All branches are assumed to be not taken
  Fetch the successor instruction and start pumping it through the pipeline stages
When the actual branch outcome is known:
  Not taken: Guessed correctly  No pipeline stall
  Taken: Guessed wrongly  Wrong instructions in the pipeline  Flush successor instruction from the pipeline

## Slide 33: 6.2 Branch Prediction: Correct Prediction
R
e
g
C
C
1
T
i
m
e
(
i
n
c
l
o
c
k
c
y
c
l
e
s
)
4
0
b
e
q
$
1
,
$
3
,
7
P
r
o
g
r
a
m
e
x
e
c
u
t
i
o
n
o
r
d
e
r
(
i
n
i
n
s
t
r
u
c
t
i
o
n
s
)
I
M
R
e
g
I
M
D
M
I
M
D
M
D
M
R
e
g
R
e
g
R
e
g
R
e
g
4
4
a
n
d
$
1
2
,
$
2
,
$
5
C
C
2
C
C
3
C
C
4
C
C
5
C
C
6
C
C
7
C
C
8
C
C
9
4
8
o
r
$
1
3
,
$
6
,
$
2
5
2
a
d
d
$
1
4
,
$
2
,
$
2
Branch is known to be not taken in cycle 3
 no stall needed!

## Slide 34: 6.2 Branch Prediction: Wrong Prediction
R
e
g
C
C
1
T
i
m
e
(
i
n
c
l
o
c
k
c
y
c
l
e
s
)
4
0
b
e
q
$
1
,
$
3
,
7
P
r
o
g
r
a
m
e
x
e
c
u
t
i
o
n
o
r
d
e
r
(
i
n
i
n
s
t
r
u
c
t
i
o
n
s
)
I
M
R
e
g
I
M
I
M
D
M
D
M
R
e
g
R
e
g
4
4
a
n
d
$
1
2
,
$
2
,
$
5
7
2
l
w
$
4
,
5
0
(
$
7
)
C
C
2
C
C
3
C
C
4
C
C
5
C
C
6
C
C
7
C
C
8
C
C
9
Bubble
Bubble
Bubble
Bubble
Branch is known to be taken in cycle 3
"and" instruction should not be executed
 Flushed from pipeline
QnA:
Q1: hi prof, can explain why is it only 1 clock cycle delay?

## Slide 35: 6.3 Reduce Stalls: Delayed Branch
Observation:
  Branch outcome takes X number of cycles to be known
  X cycles stall
Idea:
  Move non-control dependent instructions into the X slots following a branch
    Known as the branch-delay slot
  These instructions are executed regardless of the branch outcome
In our MIPS processor:
  Branch-Delay slot = 1 (with the early branch)

## Slide 36: 6.3 Delayed Branch: Example
Non-delayed branch
or $8, $9, $10
add $1, $2, $3
sub $4, $5, $6
beq $1, $4, Exit
xor $10, $1, $11
Exit:
Delayed branch
add $1, $2, $3
sub $4, $5, $6
beq $1, $4, Exit
or $8, $9, $10
xor $10, $1, $11
Exit:
The "or" instruction is moved into the delayed slot:
  Get executed regardless of the branch outcome
   Same behavior as the original code!

## Slide 37: 6.3 Delayed Branch: Observation
Best case scenario
  There is an instruction preceding the branch which can be moved into the delayed slot
    Program correctness must be preserved!
Worst case scenario
  Such instruction cannot be found
   Add a no-op (nop) instruction in the branch-delay slot
Re-ordering instructions is a common method of program optimization
  Compiler must be smart enough to do this
  Usually can find such an instruction at least 50% of the time

## Slide 38: QnA (From past semesters)

## Slide 39: Common question
In Lecture 21 Slide 24, why is the IF stage for the OR instruction in clock cycle 5? Can it not be at clock cycle 3?
Corrected chart:
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
IF | ID | EX | MEM | WB |  |  |  |  |  | 
 | IF |  |  | ID | EX | MEM | WB |  |  | 
 |  | IF |  |  | ID | EX | MEM | WB |  | 
 |  |  | IF |  |  | ID | EX | MEM | WB | 
 |  |  |  | IF |  |  | ID | EX | MEM | WB
lw
and
or
add
sw
Similar correction done to slides 21, 25 and 44.


## Slide 40: QnA Q3
Hi prof, is there any useful observation we can make to calculate the clock cycles efficiently? cus filling in the whole pipeline table does not seem practical under exam conditions.
AY2021/22 Sem1 exam
Refer to the given MIPS code. Assume a 5-stage MIPS pipeline and A[0] > B[0].
(a) How many cycles does this code segment take to complete its execution in the first iteration (I1 to I18) in an ideal pipeline?
Write the total number of additional delay cycles for each of the parts (b) to (d).
(b) Assuming without forwarding and branch decision is made at MEM stage (stage 4). No branch prediction is made.
(c) Assuming with forwarding and branch decision is made at MEM stage (stage 4). No branch prediction is made.
(d) …
add $t0, $0, $0 # I1
add $t9, $0, $0 # I2
addi $t1, $a1, 0 # I3
addi $t2, $a2, 0 # I4
sll $t8, $a0, 2 # I5
loop: slt $t3, $t0, $t8 # I6
beq $t3, $0, end # I7
lw $s1, 0($t1) # I8
lw $s2, 0($t2) # I9
slt $t3, $s1, $s2 # I10
bne $t3, $0, else # I11
add $t9, $t9, $s1 # I12
j cont # I13
else: sub $t9, $t9, $s2 # I14
cont: addi $t0, $t0, 4 # I15
addi $t1, $t1, 4 # I16
addi $t2, $t2, 4 # I17
j loop # I18
end:

## Slide 41: QnA Q3
Hi prof, is there any useful observation we can make to calculate the clock cycles efficiently? cus filling in the whole pipeline table does not seem practical under exam conditions.
AY2021/22 Sem1 exam
Refer to the given MIPS code. Assume a 5-stage MIPS pipeline and A[0] > B[0].
(a) How many cycles does this code segment take to complete its execution in the first iteration (I1 to I18) in an ideal pipeline?
Write the total number of additional delay cycles for each of the parts (b) to (d).
(b) Assuming without forwarding and branch decision is made at MEM stage (stage 4). No branch prediction is made.
(c) Assuming with forwarding and branch decision is made at MEM stage (stage 4). No branch prediction is made.
(d) …
(b) (c) (d)
add $t0, $0, $0 # I1
add $t9, $0, $0 # I2
addi $t1, $a1, 0 # I3
addi $t2, $a2, 0 # I4
sll $t8, $a0, 2 # I5
loop: slt $t3, $t0, $t8 # I6 +2
beq $t3, $0, end # I7 +2
lw $s1, 0($t1) # I8 +3 +3
lw $s2, 0($t2) # I9
slt $t3, $s1, $s2 # I10 +2 +1
bne $t3, $0, else # I11 +2
add $t9, $t9, $s1 # I12 +3 +3
j cont # I13
else: sub $t9, $t9, $s2 # I14
cont: addi $t0, $t0, 4 # I15 +1 +1
addi $t1, $t1, 4 # I16
addi $t2, $t2, 4 # I17
j loop # I18
end:
Total: +15 +8

## Slide 42: PIPELINING QUIZ

## Slide 43
Pipelining Quiz Question 1
Let’s say there are 6 stages in executing an instruction and there are 10 instructions in a program. Each stage takes 1 clock cycle to execute. How many clock cycles are needed to complete the execution of this program in an ideal pipeline?
I = no. of instructions
N = no. of pipeline stages
I + N – 1 = 10 + 6 – 1 = 15 cycles


## Slide 44
Pipelining Quiz Question 2
Pipeline register can store which of the following?









## Slide 45
Pipelining Quiz Question 3
Each of the pipeline registers contains multiple registers of size 32 bits?



## Slide 46
Pipelining Quiz Question 4
The MIPS processor that we discussed in this course can execute at most 4 instructions simultaneously in an ideal pipeline.



## Slide 47
Pipelining Quiz Question 5
Below is a sequence of instructions A to F:
A. lw $t2, 0($t1)
B. lw $t1, 100($t6)
C. sub $t6, $t1, $t2
D. add $t6, $t2, $t6
E. and $t3, $t6, $0
F. sw $t6, 50($t1)
Which of the following are true with respect to RAW, WAR and WAW data dependency?






## Slide 48
Pipelining Quiz Question 6
How many cycles are needed to execute this program with and without forwarding?
A. lw $t2, 0($t1)
B. lw $t1, 100($t6)
C. sub $t6, $t1, $t2
D. add $t6, $t2, $t6
E. and $t3, $t6, $0
F. sw $t6, 50($t1)
Without forwarding:
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
lw | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  | 
lw |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
sub |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
and |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
sw |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
With forwarding:
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
lw | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  | 
lw |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
sub |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
and |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
sw |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
F D E M W
F D E M W
F D E M W
F D E M W
F D E M W
16 cycles
F D E M W
F D E M W
F D E M W
F D E M W
F D E M W
11 cycles


## Slide 49
Pipelining Quiz Question 7
How many cycles are needed to execute this program with forwarding, assume branch-taken prediction strategy, branch decision made at MEM, whereas the actual branch in the code is taken.
lw $s2, 0($s1)
bne $s2, $s3, L1
sub $s0, $s4, $s5
L1: add $s0, $s0, $s3
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
lw | F | D | E | M | W |  |  |  |  |  |  | 
bne |  |  |  |  |  |  |  |  |  |  |  | 
add |  |  |  |  |  |  |  |  |  |  |  | 
F D E M W
F D E M W
8 cycles


## Slide 50
Pipelining Quiz Question 8
How many cycles are needed to execute this program with forwarding, assume branch-NOT-taken prediction strategy, branch decision made at MEM, whereas the actual branch in the code is taken.
lw $s2, 0($s1)
bne $s2, $s3, L1
sub $s0, $s4, $s5
L1: add $s0, $s0, $s3
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
lw | F | D | E | M | W |  |  |  |  |  |  | 
bne |  |  |  |  |  |  |  |  |  |  |  | 
sub |  |  |  |  |  |  |  |  |  |  |  | 
add |  |  |  |  |  |  |  |  |  |  |  | 
add |  |  |  |  |  |  |  |  |  |  |  | 
F D E M W
F D E M W
F D E M W
F D E M W
11 cycles


## Slide 51: Past YEARs’ QUESTIONS
Pipelining
AY2020/21 Sem2 Q16
AY2023/24 Sem1 Q16

## Slide 52: AY2020/21 Sem2 Q16(a)
Answer: 16 + (5 – 1) = 20


## Slide 53: AY2020/21 Sem2 Q16(b)
(b)
+2
+2
+3
+2
+2
+2
+2
+3
+2
+2
+2
24


## Slide 54: AY2020/21 Sem2 Q16(c)
(b)
+2
+2
+3
+2
+2
+2
+2
+3
+2
+2
+2
24
(c)
+2
+2
+1
+2
+2
+2
+2
+1
+2
+2
+2
22


## Slide 55: AY2020/21 Sem2 Q16(d)
(b)
+2
+2
+3
+2
+2
+2
+2
+3
+2
+2
+2
24
(c)
+2
+2
+1
+2
+2
+2
+2
+1
+2
+2
+2
22
(d)
+1
+1
+1
+1
4


## Slide 56: AY2020/21 Sem2 Q16(e)
(b)
+2
+2
+3
+2
+2
+2
+2
+3
+2
+2
+2
24
(c)
+2
+2
+1
+2
+2
+2
+2
+1
+2
+2
+2
22
(d)
+1
+1
+1
+1
4
More than 1 possible answer.
Move I14 (addi $s5, $s5, 1) to between I11 (lw $s4, 0($t4)) and I12 (sub $s3, $s3, $s4) to remove the 1 cycle of delay at I12.
If your answer involves I15, explain where the label “skip” goes to.


## Slide 57: AY2023/24 Sem1 Q16(a)
8 (i.e. $8)


## Slide 58: AY2023/24 Sem1 Q16(b)
40 cycles


## Slide 59: AY2023/24 Sem1 Q16(c)
29 cycles


## Slide 60: AY2023/24 Sem1 Q16(d)
27 cycles


## Slide 61: Additional Exercise

## Slide 62: Additional Exercise: Tracing signals and data
Using Powerpoint animation, give the full details of the signals and data bits (highlighting those lines that are active) of the following code that is executed in a pipelined MIPS. Assume that L is at address 0x00000100 and the beq instruction is at address 0x00001000.
sub $1, $2, $3
lw $6, 4($7)
beq $4, $5, L
Credit: A/P Anandha Gopalan
0x00430822
0x8CE60004
0x1085FC3F
encoding

## Slide 63
PC= 0xFFC
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
RegWrite
MemWrite
MemRead
MemtoReg
RegDst
ALUOp
ALUSrc
Branch
PCSrc
sub $1, $2, $3
PC= 0xFF8
0x00430822
Q1
sub $1, $2, $3
lw $6, 4($7)
beq $4, $5, L
L at 0x00000100
beq inst at 0x00001000

## Slide 64
RegWrite = 1
MemtoReg = 0
PC= 0x1000
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
RegWrite
MemWrite
MemRead
MemtoReg
RegDst
ALUOp
ALUSrc
Branch
PCSrc
lw $6, 4($7)
PC= 0xFFC
0x8CE60004
sub $1, $2, $3
2
3
RegDst = 1
ALUOp = 2
ALUSrc = 0
Q1
Branch = 0
MemRead = 0
MemWrite = 0
sub $1, $2, $3
lw $6, 4($7)
beq $4, $5, L
L at 0x00000100
beq inst at 0x00001000

## Slide 65
RegWrite = 1
MemtoReg = 1
PC= 0x1004
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
RegWrite
MemWrite
MemRead
MemtoReg
RegDst
ALUOp
ALUSrc
Branch
PCSrc
lw $6, 4($7)
PC= 0x1000
0x1085FC3F
beq $4, $5, L
7
X
RegDst = 0
ALUOp = 0
ALUSrc = 1
RegWrite = 1
MemtoReg = 0
Branch = 0
MemRead = 0
MemWrite = 0
sub $1, $2, $3
0
1
2
Q1
Branch = 0
MemRead = 1
MemWrite = 0
sub $1, $2, $3
lw $6, 4($7)
beq $4, $5, L
L at 0x00000100
beq inst at 0x00001000

## Slide 66
RegWrite = 0
MemtoReg = X
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
RegWrite
MemWrite
MemRead
MemtoReg
RegDst
ALUOp
ALUSrc
Branch
PCSrc
lw $6, 4($7)
beq $4, $5, L
4
5
RegDst = X
ALUOp = 2
ALUSrc = 0
RegWrite = 1
MemtoReg = 1
Branch = 0
MemRead = 1
MemWrite = 0
sub $1, $2, $3
1
0
0
RegWrite = 1
MemtoReg = 0
0
0
0
Q1
Branch = 1
MemRead = 0
MemWrite = 0
sub $1, $2, $3
lw $6, 4($7)
beq $4, $5, L
L at 0x00000100
beq inst at 0x00001000

## Slide 67
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
RegWrite
MemWrite
MemRead
MemtoReg
RegDst
ALUOp
ALUSrc
Branch
PCSrc
lw $6, 4($7)
beq $4, $5, L
RegWrite = 0
MemtoReg = X
Branch = 1
MemRead = 0
MemWrite = 0
sub $1, $2, $3
1
0
0
RegWrite = 1
MemtoReg = 1
0
0
1
1
0
1
Q1
sub $1, $2, $3
lw $6, 4($7)
beq $4, $5, L
L at 0x00000100
beq inst at 0x00001000

## Slide 68
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
RegWrite
MemWrite
MemRead
MemtoReg
RegDst
ALUOp
ALUSrc
Branch
PCSrc
lw $6, 4($7)
beq $4, $5, L
RegWrite = 0
MemtoReg = X
1
0
0
1
1
6
0x100
Q1
sub $1, $2, $3
lw $6, 4($7)
beq $4, $5, L
L at 0x00000100
beq inst at 0x00001000

## Slide 69
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
RegWrite
MemWrite
MemRead
MemtoReg
RegDst
ALUOp
ALUSrc
Branch
PCSrc
beq $4, $5, L
0
X
Q1
sub $1, $2, $3
lw $6, 4($7)
beq $4, $5, L
L at 0x00000100
beq inst at 0x00001000

## Slide 70
Next week – Final recitation!
Cache

## Slide 71: End of File