## Slide 1: https://www.comp.nus.edu.sg/~cs2100/
CS2100
Recitation 12
Cache
13 April 2026
Aaron Tan

## Slide 2: Contents
Cache Revision
Past year’s exam question
  AY2021/22 Sem1 Q16
Cache Quiz
Final Exam

## Slide 4: Memory Hierarchy
Cache is 10 to 100 times faster than main memory
Main memory (~60ns to 100ns)
Cache
  L1 cache: ~0.5 – 1 ns
  L2 cache: ~3 – 10 ns
  L3 cache: ~10 – 40 ns

## Slide 5: Temporal & Spatial Locality
Example: 4-byte words, 4-word cache blocks.
A[0][0] | A[0][1] | A[0][2] | A[0][3]
A[1][0] | A[1][1] | A[1][2] | A[1][3]
A[2][0] | A[2][1] | A[2][2] | A[2][3]
34 integer array A

## Slide 6: Direct Mapped Cache - Basics
Cache blocks/Line
Block Size
Block Number
Offset
Cache Index
Tag
Block no.
Byte Offset

## Slide 7: Direct Mapped Cache - Basics
Cache blocks/Line
Block Size
Block Number
Offset
Cache Index
Tag
Mapping Function:
Cache Index
= (BlockNumber) modulo
(NumberOfCacheBlocks)
Observation:
If Number of Cache Blocks = 2M
 the last M bits of the block number is the cache index
Example:
Cache has 22 = 4 blocks
 last 2 bits of the block number is the cache index.
Index
00
01
10
11
Cache Index
Cache
One block
..00000
..00001
..00010
..00011
..00100
..00101
..00110
..00111
..01000
..01001
..01010
..01011
..01100
..01101
..01110
..01111
Block Number (Not Address!)
Memory
One block

## Slide 8: Direct Mapped Cache - Basics
Cache blocks/Line
Block Size
Block Number
Offset
Cache Index
Tag
Mapping Function:
Cache Index
= (BlockNumber) modulo
(NumberOfCacheBlocks)
Observation:
Multiple memory blocks can map to the same cache block
 Same Cache Index
However, they have unique tag number:
Tag = Block number / Number of Cache Blocks
Memory
..00000
..00001
..00010
..00011
..00100
..00101
..00110
..00111
..01000
..01001
..01010
..01011
..01100
..01101
..01110
..01111
Block Number (Not Address!)
One block
00
01
10
11
Cache Index
Cache
One block
Tag

## Slide 9: Direct Mapped Cache - Basics
Memory address
  Tag
  Index
  Byte Offset

## Slide 10: Direct Mapped Cache - Basics
Cache
00
01
10
11
Index
Data
Tag
Valid
Along with a data block (line), cache also contains the following administrative information (overheads):
Tag of the memory block
Valid bit indicating whether the cache line contains valid data
When is there a cache hit?
( Valid[index] = TRUE ) AND ( Tag[ index ] = Tag[ memory address ] )

## Slide 11: Direct Mapped Cache - Example
Memory
4GB
Memory Address
31
0
N-1
N
Block Number
Offset
1 Block
= 16 bytes
Cache
16KB
1 Block
= 16 bytes
N+M-1
31
0
N-1
N
Tag
Offset
Index
Offset, N = 4 bits
Block Number = 32 – 4 = 28 bits
Check: Number of Blocks = 228
Number of Cache Blocks
= 16KB / 16bytes = 1024 = 210
Cache Index, M = 10bits
Cache Tag = 32 – 10 – 4 = 18 bits

## Slide 12: Direct Mapped Cache - Example

## Slide 13: 5. Reading Data: Setup
Given a direct mapped 16KB cache:
  16-byte blocks x 1024 cache blocks
Trace the following memory accesses:
13
31
0
3
4
000000000000000000
0100
Tag
Offset
0000000001
Index
14
000000000000000000
1100
0000000001
000000000000000000
0100
0000000011
000000000000000010
1000
0000000001
000000000000000000
0000
0000000001
Direct Mapped Cache

## Slide 14: 5. Reading Data: Initial State
Intially cache is empty
   All valid bits are zeroes (false)
0
0
0
0
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Index
Direct Mapped Cache

## Slide 15: 5. Reading Data: Load #1-1
0
0
0
0
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Index
Load from
Step 1. Check Cache Block at index 1
000000000000000000
0100
Tag
Offset
0000000001
Index
Direct Mapped Cache

## Slide 16: 5. Reading Data: Load #1-2
Load from
Step 2. Data in block 1 is invalid [Cold/Compulsory Miss]
000000000000000000
0100
Tag
Offset
0000000001
Index
0
0
0
0
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Index
Direct Mapped Cache

## Slide 17: 5. Reading Data: Load #1-3
Load from
Step 3. Load 16 bytes from memory; Set Tag and Valid bit
000000000000000000
0100
Tag
Offset
0000000001
Index
0
0
1
A
B
C
D
0
0
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Index
Direct Mapped Cache

## Slide 18: 5. Reading Data: Load #1-4
Load from
Step 4. Return Word1 (byte offset = 4) to Register
000000000000000000
0100
Tag
Offset
0000000001
Index
0
0
1
A
B
C
D
0
0
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Index
Direct Mapped Cache

## Slide 19: 5. Reading Data: Load #2-1
Load from
Step 1. Check Cache Block at index 1
000000000000000000
1100
Tag
Offset
0000000001
Index
0
0
1
A
B
C
D
0
0
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Index
Direct Mapped Cache

## Slide 20: 5. Reading Data: Load #2-2
Load from
Step 2. [Cache Block is Valid] AND [Tags match]  Cache hit!
000000000000000000
1100
Tag
Offset
0000000001
Index
0
0
1
A
B
C
D
0
0
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Index
Direct Mapped Cache

## Slide 21: 5. Reading Data: Load #2-3
Load from
Step 3. Return Word3 (byte offset = 12) to Register [Spatial Locality]
000000000000000000
1100
Tag
Offset
0000000001
Index
0
0
1
A
B
C
D
0
0
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Index
Direct Mapped Cache

## Slide 22: 5. Reading Data: Load #3-1
Load from
Step 1. Check Cache Block at index 3
000000000000000000
0100
Tag
Offset
0000000011
Index
0
0
1
A
B
C
D
0
0
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Index
Direct Mapped Cache

## Slide 23: 5. Reading Data: Load #3-2
Load from
Step 2. Data in block 3 is invalid [Cold/Compulsory Miss]
000000000000000000
0100
Tag
Offset
0000000011
Index
0
0
1
A
B
C
D
0
0
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Index
Direct Mapped Cache

## Slide 24: 5. Reading Data: Load #3-3
Load from
Step 3. Load 16 bytes from memory; Set Tag and Valid bit
000000000000000000
0100
Tag
Offset
0000000011
Index
0
0
1
A
B
C
D
0
0
1
I
J
K
L
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Index
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Direct Mapped Cache

## Slide 25: 5. Reading Data: Load #3-4
Load from
Step 4. Return Word1 (byte offset = 4) to Register
000000000000000000
0100
Tag
Offset
0000000011
Index
0
0
1
A
B
C
D
0
0
1
I
J
K
L
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Index
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Direct Mapped Cache

## Slide 26: 5. Reading Data: Load #4-1
Load from
Step 1. Check Cache Block at index 1
000000000000000010
1000
Tag
Offset
0000000001
Index
0
0
1
A
B
C
D
0
0
1
I
J
K
L
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Index
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Direct Mapped Cache

## Slide 27: 5. Reading Data: Load #4-2
Load from
Step 2. Cache block is Valid but Tags mismatch [Cold miss]
000000000000000010
1000
Tag
Offset
0000000001
Index
0
0
1
A
B
C
D
0
0
1
I
J
K
L
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Index
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Direct Mapped Cache

## Slide 28: 5. Reading Data: Load #4-3
Load from
Step 3. Replace block 1 with new data; Set Tag
000000000000000010
1000
Tag
Offset
0000000001
Index
0
2
1
E
F
G
H
0
0
1
I
J
K
L
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Index
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Direct Mapped Cache

## Slide 29: 5. Reading Data: Load #4-4
Load from
Step 4. Return Word2 (byte offset = 8) to Register
000000000000000010
1000
Tag
Offset
0000000001
Index
0
2
1
E
F
G
H
0
0
1
I
J
K
L
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Index
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Direct Mapped Cache

## Slide 30: 5. Reading Data: Load #5-1
Load from
Step 1. Check Cache Block at index 1
000000000000000000
0000
Tag
Offset
0000000001
Index
0
2
1
E
F
G
H
0
0
1
I
J
K
L
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Index
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Direct Mapped Cache

## Slide 31: 5. Reading Data: Load #5-2
Load from
Step 2. Cache block is Valid but Tags mismatch [Cold miss]
000000000000000000
0000
Tag
Offset
0000000001
Index
0
2
1
E
F
G
H
0
0
1
I
J
K
L
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Index
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Direct Mapped Cache

## Slide 32: 5. Reading Data: Load #5-3
Load from
Step 3. Replace block 1 with new data; Set Tag
000000000000000000
0000
Tag
Offset
0000000001
Index
0
0
1
A
B
C
D
0
0
1
I
J
K
L
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Index
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Direct Mapped Cache

## Slide 33: 5. Reading Data: Load #5-4
Load from
Step 4. Return Word0 (byte offset = 0) to Register
000000000000000000
0000
Tag
Offset
0000000001
Index
0
0
1
A
B
C
D
0
0
1
I
J
K
L
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Index
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Direct Mapped Cache

## Slide 34: 3. Set Associative (SA) Cache
N-way Set Associative Cache
  A memory block can be placed in a fixed number (N) of locations in the cache, where N > 1
Key Idea:
  Cache consists of a number of sets:
    Each set contains N cache blocks
  Each memory block maps to a unique cache set
  Within the set, a memory block can be placed in any of the N cache blocks in the set

## Slide 35: 3. Set Associative Cache: Structure
An example of 2-way set associative cache
  Each set has two cache blocks
A memory block maps to a unique set
  In the set, the memory block can be placed in either of the cache blocks
   Need to search both blocks in the set to look for the memory block
2-way Set Associative Cache
00
01
10
11
Set Index
Data
Tag
Valid
Data
Tag
Valid
Set

## Slide 36: 3. Set Associative Cache: Mapping
Cache Block size = 2N bytes
Number of cache sets = 2M
Offset = N bits
Set Index = M bits
Tag = 32 – (N + M) bits
Cache Block size = 2N bytes
Memory Address
31
0
N-1
N
Block Number
Offset
N+M-1
31
0
N-1
N
Tag
Offset
Set Index
Cache Set Index
= (BlockNumber) modulo (NumberOfCacheSets)
Observation:
It is essentially unchanged from the direct-mapping formula

## Slide 37: 3. Set Associative Cache: Example
Memory
4GB
Memory Address
31
0
N-1
N
Block Number
Offset
1 Block
= 4 bytes
N+M-1
31
0
N-1
N
Tag
Offset
Set Index
Offset, N = 2 bits
Block Number = 32 – 2 = 30 bits
Check: Number of Blocks = 230
Number of Cache Blocks
= 4KB / 4bytes = 1024 = 210
4-way associative, number of sets
= 1024 / 4 = 256 = 28
Set Index, M = 8 bits
Cache Tag = 32 – 8 – 2 = 22 bits
Cache
4 KB

## Slide 38: Direct Mapped Cache vs 2-way Set Assoc Cache

## Slide 39: 4-way Set Associative Cache

## Slide 40: 4. Fully Associative (FA) Cache
Fully Associative Cache
  A memory block can be placed in any location in the cache
Key Idea:
  Memory block placement is no longer restricted by cache index or cache set index
  ++ Can be placed in any location, BUT
  --- Need to search all cache blocks for memory access

## Slide 41: 4. Fully Associative Cache: Mapping
Cache Block size = 2N bytes
Number of cache blocks = 2M
Offset = N bits
Tag = 32 – N bits
Cache Block size = 2N bytes
Memory Address
31
0
N-1
N
Block Number
Offset
31
0
N-1
Tag
Offset
Observation:
The block number serves as the tag in FA cache.
N

## Slide 42: Fully Associative Cache

## Slide 43: 5. Block Replacement Policy (1/3)
Set Associative or Fully Associative Cache:
  Can choose where to place a memory block
  Potentially replacing another cache block if full
  Need block replacement policy
Least Recently Used (LRU)
  How: For cache hit, record the cache block that was accessed
    When replacing a block, choose one which has not been accessed for the longest time
  Why: Temporal locality

## Slide 44: 5. Block Replacement Policy (2/3)
Least Recently Used policy in action:
  4-way SA cache
  Memory accesses: 0 4 8 12 4 16 12 0 4
8
12
4
16
4
16
12
0
0
4
8
12
LRU
0
8
12
4
8
4
16
12
16
12
0
4
Hit
Miss (Evict Block 0)
Hit
Miss (Evict Block 8)
Hit
Access 4
Access 16
Access 12
Access 0
Access 4
x
x

## Slide 45: 5. Block Replacement Policy (3/3)
Drawback for LRU
  Hard to keep track if there are many choices
Other replacement policies:
  First in first out (FIFO)
  Random replacement (RR)
  Least frequently used (LFU)

## Slide 46: Types of Cache Misses
Compulsory misses
  On the first access to a block; the block must be brought into the cache
  Also called cold start misses or first reference misses
Conflict misses
  Occur in the case of direct mapped cache or set associative cache, when several blocks are mapped to the same block/set
  Also called collision misses or interference misses
Capacity misses
  Occur when blocks are discarded from cache as cache cannot contain all blocks needed

## Slide 47: Handling Misses
On a Read Miss:
  Data loaded into cache and then load from there to register
Write Miss option 1: Write allocate
  Load the complete block into cache
  Change only the required word in cache
  Write to main memory depends on write policy (write-through or write-back)
Write Miss option 2: Write around
  Do not load the block to cache
  Write directly to main memory only

## Slide 48: Write Policy in Cache
Cache and main memory are inconsistent
  Modified data only in cache, not in memory!
Solution 1: Write-through cache
  Write data both to cache and to main memory
Solution 2: Write-back cache
  Only write to cache
  Write to main memory only when cache block is replaced (evicted)

## Slide 49: Cache Summary

## Slide 50: Cache Summary

## Slide 51: Cache Summary

## Slide 52: IMPORTANT MESSAGES

## Slide 53: Important #1: Academic Offence
Number of cases of cheating in assessments (midterm tests, exams) has gone up.
Real examples:
  Student continued to write after the “stop writing” instruction was given, claiming that he did not hear the announcement.
  Student brought in unauthorized materials.
  Student went to the toilet with his mobile phone and accessed AI tool.
  Student (blatantly) used mobile phone in the exam hall during the exam!
The university treats such offences very seriously.
Most likely minimum penalty: fail the course right away
  Possible impacts: Barred from being a tutor/going for SEP/special programmes, etc.
Investigation may take a long time: stressed for a prolonged period.

## Slide 54: Important #2: Falling Sick Before/During Exam Period
Final exams are administered centrally by OUR, not by the individual schools/faculties.
There are no make-up final exams.
If you fall sick, you may submit a Special Consideration application via StuRec, with documentary support (eg: medical certificate).
  Likely outcome: If your application is approved (by the board), you may be offered the choice of accepting your grade based on your CA, or an IC (incomplete) grade.
  IC grade is not a pass grade; you have to retake the course if it is an essential course.
Please keep yourself HEALTHY before the exam period!!!

## Slide 55: AY2021/22 Semester 1 Exam Q16

## Slide 56: AY2021/22 Sem1 Q16

## Slide 57: AY2021/22 Sem1 Q16

## Slide 58
add $t0, $0, $0 # I1
add $t9, $0, $0 # I2
addi $t1, $a1, 0 # I3
addi $t2, $a2, 0 # I4
sll $t8, $a0, 2 # I5
loop: slt $t3, $t0, $t8 # I6
beq $t3, $0, end # I7
lw $s1, 0($t1) # I8
lw $s2, 0($t2) # I9
slt $t3, $s1, $s2 # I10
bne $t3, $0, else # I11
add $t9, $t9, $s1 # I12
j cont # I13
else: sub $t9, $t9, $s2 # I14
cont: addi $t0, $t0, 4 # I15
addi $t1, $t1, 4 # I16
addi $t2, $t2, 4 # I17
j loop # I18
end:
Direct-mapped data cache with 512 words in total and each block contains 8 words.
You may assume:
Array A starts at address 0xCDEF 0400.
Array B follows immediately after array A in the memory.
for (answer=0, k=0; k<size; k++) {
if (A[k]>=B[k]) answer += A[k];
else answer -= B[k];
}
(a) How many bits are there in the index field? Byte offset field?
Number of blocks = 512/8 = 64 = 26.
Therefore, index field: 6 bits.
Number of bytes in a block = 84 = 32 = 25.
Therefore, byte offset field: 5 bits.


## Slide 59
Direct-mapped data cache with 512 words in total and each block contains 8 words.
You may assume:
Array A starts at address 0xCDEF 0400.
Array B follows immediately after array A in the memory.
for (answer=0, k=0; k<size; k++) {
if (A[k]>=B[k]) answer += A[k];
else answer -= B[k];
}
(b) Arrays A and B each has 1032 elements. What is the hit rate for arrays A and B?
Index: 6 bits
Byte offset: 5 bits
Array A start addr = 0xCDEF 0400
= 0b … 0000 0100 0000 0000.
Therefore, A[0] resides in word 0 of block 32.
A[1024] to A[1031] will occupy block 32.
Therefore, B[0] will occupy word 0 of block 33.
No cache trashing. For every 8 elements, the first is a miss and the rest are hits.
Therefore, hit rate is 7/8 for both arrays.
A0 | A1 | A2 | A3 | A4 | A5 | A6 | A7
B0 | B1 | B2 | B3 | B4 | B5 | B6 | B7
Block
32
33


## Slide 60
Direct-mapped data cache with 512 words in total and each block contains 8 words.
You may assume:
Array A starts at address 0xCDEF 0400.
Array B follows immediately after array A in the memory.
(c) Arrays A and B each has 1028 elements. What is the hit rate for arrays A and B?
Index: 6 bits
Byte offset: 5 bits
Array A start addr = 0xCDEF 0400
= 0b … 0000 0100 0000 0000.
Therefore, A[0] resides in word 0 of block 32.
A[1024] to A[1027] will occupy the first 4 words of block 32, and B[0] to B[3] will occupy the next 4 words in the same block.
Therefore, for every 8 elements, the first 5 will be misses and the next 3 are hits, and this applies to the first 1024 elements. For the last 4 elements, they are all misses due to thrashing.
Hence, there are 3/8  1024 = 384 hits altogether for each array.
Therefore, hit rate = 384/1028.
A1024 | A1025 | A1026 | A1027 | B0 | B1 | B2 | B3
Block
32
Snapshot of first 16 elements:
Block 32 | A0 (M) | A1 (M) | A2 (M) | A3 (M) | A4 (M) B0 (M) | A5 (H) B1 (M) | A6 (H) B2 (M) | A7 (H) B3 (M)
Block 33 | B4 (M) A8 (M) | B5 (H) A9 (M) | B6 (H) A10 (M) | B7 (H) A11 (M) | B8 (M) A12 (M) | B9 (M) A13 (H) | B10 (M) A14 (H) | B11 (M) A15 (H)
Block 34 | B12 (M) | B13 (H) | B14 (H) | B15 (H) |  |  |  | 


## Slide 61
Direct-mapped data cache with 512 words in total and each block contains 8 words.
You may assume:
Array A starts at address 0xCDEF 0400.
Array B follows immediately after array A in the memory.
(d) Assuming that arrays A and B have at least 100 elements each, (i) what is the lowest hit rate possible for array A? (ii) how many elements in array A would result in this lowest hit rate?
Index: 6 bits
Byte offset: 5 bits
(i) Lowest hit rate is 0. This occurs when there is cache trashing, i.e. the first elements of array A and array B are mapped to the same cache location.
(ii) When array A has a multiple of 512 elements (this is the simplest answer).


## Slide 62
add $t0, $0, $0 # I1
add $t9, $0, $0 # I2
addi $t1, $a1, 0 # I3
addi $t2, $a2, 0 # I4
sll $t8, $a0, 2 # I5
loop: slt $t3, $t0, $t8 # I6
beq $t3, $0, end # I7
lw $s1, 0($t1) # I8
lw $s2, 0($t2) # I9
slt $t3, $s1, $s2 # I10
bne $t3, $0, else # I11
add $t9, $t9, $s1 # I12
j cont # I13
else: sub $t9, $t9, $s2 # I14
cont: addi $t0, $t0, 4 # I15
addi $t1, $t1, 4 # I16
addi $t2, $t2, 4 # I17
j loop # I18
end:
2-way set associative instruction cache with LRU replacement policy. You may assume:
Array A and array B each contains 100 elements.
Array A contains +ve values, array B contains -ve values.
Instruction I1 is stored at address 0x2B00 0FFC.
(e) The instruction cache contains 16 words in total and each block contains 4 words.
Number of sets = 16/4/2 = 2 = 21.
Therefore, set index field: 1 bit.
Number of bytes in a block = 44 = 16 = 24.
Therefore, byte offset field: 4 bits.
(i) How many bits in the set index field? In the byte offset field?
for (answer=0, k=0; k<size; k++) {
if (A[k]>=B[k]) answer += A[k];
else answer -= B[k];
}


## Slide 63
add $t0, $0, $0 # I1
add $t9, $0, $0 # I2
addi $t1, $a1, 0 # I3
addi $t2, $a2, 0 # I4
sll $t8, $a0, 2 # I5
loop: slt $t3, $t0, $t8 # I6
beq $t3, $0, end # I7
lw $s1, 0($t1) # I8
lw $s2, 0($t2) # I9
slt $t3, $s1, $s2 # I10
bne $t3, $0, else # I11
add $t9, $t9, $s1 # I12
j cont # I13
else: sub $t9, $t9, $s2 # I14
cont: addi $t0, $t0, 4 # I15
addi $t1, $t1, 4 # I16
addi $t2, $t2, 4 # I17
j loop # I18
end:
Addr of I1 = 0x2B00 0FFC = 0b… 1111 1100.
So I1 is stored in set 1, word 3.
1st iteration: I1 – I13, I15 – I18;
2nd – 100th: I6 – I13, I15 – I18; winding up: I6 and I7.
(ii) How many misses are there?
2-way set associative instruction cache with LRU replacement policy. You may assume:
Array A and array B each contains 100 elements.
Array A contains +ve values, array B contains -ve values.
Instruction I1 is stored at address 0x2B00 0FFC.
(e) The instruction cache contains 16 words in total and each block contains 4 words.
I2 (M) I18 (M) | I3 (H) | I4 (H) | I5 (H) | I10 (M) | I11 (H) | I12 (H) | I13 (H)
 | I15 (M) | I16 (H) | I1 (M) I17 (H) | I6 (M) | I7 (H) | I8 (H) | I9 (H)
Set 0
Set 1
6 misses in 1st iteration, thereafter all hits.


## Slide 64
Addr of I1 = 0x2B00 0FFC = 0b… 1111 1100.
So I1 is stored in set 3, word 1.
1st iteration: I1 – I13, I15 – I18;
2nd – 100th: I6 – I13, I15 – I18; winding up: I6 and I7.
2-way set associative instruction cache with LRU replacement policy. You may assume:
Array A and array B each contains 100 elements.
Array A contains +ve values, array B contains -ve values.
Instruction I1 is stored at address 0x2B00 0FFC.
(f) The instruction cache contains 16 words in total and each block contains 2 words. How many misses are there?
I2 (M) I18 (M) | I3 (H) | I10 (M) | I11 (H)
I4 (M) | I5 (H) | I12 (M) | I13 (H)
I6 (M) | I7 (H) |  | I15 (M)
I16 (M) | I1 (M) I17 (H) | I8 (M) | I9 (H)
10 misses in 1st iteration, thereafter all hits.
Set index: 2 bits
Byte offset: 3 bits
Set 0
Set 1
Set 2
Set 3


## Slide 65: CACHE QUIZ

## Slide 66: Cache Quiz Question 1
For a memory with size 4GB, each block is 32 bytes. The size of the cache is 32KB with the same block size. Fill in the following with respect to Direct Mapping Cache:
How many bytes per block? 32 = 25
log2(32) = 5
Memory size = 4GB = 232 bytes. Hence address has 32 bits, out of which 5 bits are used for offset.
32 – 5 = 27
How many blocks in cache? 32KB/32 = (32210)/32 = 210
10
Tag size = address size – index size – byte offset size
32 – 10 – 5 = 17
1024
0x12345678
= 0b 0001 0010 0011 0100 0101 0110 0111 1000
0b00010010001101000
0b1010110011
0b11000
210 = 1024


## Slide 67: Cache Quiz Question 2
Consider a 4-way set associative mapped cache with block size 4KB. The size of the main memory is 16GB and there are 10 bits in the tag. Find the number of sets in the cache and the size of the cache.
Memory size = 16GB = 234 bytes. Hence address has 34 bits.
Size of one block = 4KB = 212 bytes. Therefore, byte offsets = 12 bits.
No. of set index bits = address size – tag size – byte offset size
= 34 – 10 – 12 = 12.
Therefore, number of sets = 212.
212
Size of each cache set = 4  block size = 4  4KB = 16KB = 214 bytes.
Therefore, cache size = 212  214 bytes = 226 bytes = 26 MB = 64MB.
64


## Slide 68: Cache Quiz Question 3
Given a fully set associative cache. The size of the main memory is 256MB, size of cache memory is 16KB and the block size is 256bytes. Find the number of bit for byte offset and tag.
Memory size = 256MB = 228 bytes. Hence address has 28 bits.
Block size = 256 bytes = 28 bytes.
8
28 – 8 = 20


## Slide 69: FINAL EXAM

## Slide 70: Final Exam (AY2025/26 semester 2)
30 April 2026, Thursday, 1 – 3pm
MPSH2B and MPSH4
Earlier topics (30%)
Later topics (70%)
Format:
17 MCQs (34 marks)
6 multi-parts questions (66 marks)

## Slide 71: Final Exam (AY2025/26 semester 2)
Bring your pencils (2B or above), eraser, writing papers.
Shade your Student Number correctly (and check!) using pencil.
Shade the MCQ answers using pencil.
Do NOT write your answers outside the boxes provided.

## Slide 72: End of File