## Slide 1: https://www.comp.nus.edu.sg/~cs2100/
CS2100 Recitation 8
Combinational Circuits
16 March 2026
Aaron Tan

## Slide 2: Contents
Design Methods
    Gate-level design method
    Block-level design method
Magnitude Comparator
Circuit Delays
Quizzes
Selected Past Years’ Exam Questions
AY2020/21 Sem2 Q13(d)
AY2021/22 Sem1 Q13(a)
AY2021/22 Sem2 Q14(b)(c)
AY2023/24 Sem1 Q17(a)(b)(d)

## Slide 3
Feedback
Students expressed wish for shorter recitation sessions
I’ve cut down the materials, replacing with problem solving questions using past years’ exam questions.

## Slide 4
ANDROID
NANDROID
NOTDROID
ORDROID

## Slide 5: summary
Design Methods

## Slide 6: 1. Introduction
Two classes of logic circuits
Combinational Circuit
  Each output depends entirely on the immediate (present) inputs.
Combinational
Logic
: :
inputs
outputs
: :
Sequential Circuit
  Each output depends on both present inputs and state.
Memory
Combinational
Logic
: :
inputs
outputs
: :
This week and next week.
Week 11.
Design methods
  Gate-level design method (with logic gates)
  Block-level design method (with functional blocks)

## Slide 7: 4. BCD to Excess-3 Code Converter (1/3)
Digit | BCD code (8421 code) | Excess-3 code
0 | 0000 | 0011
1 | 0001 | 0100
2 | 0010 | 0101
3 | 0011 | 0110
4 | 0100 | 0111
5 | 0101 | 1000
6 | 0110 | 1001
7 | 0111 | 1010
8 | 1000 | 1011
9 | 1001 | 1100
Other decimal codes we used to cover:
84-2-1 code
0000
0111
0110
0101
0100
1011
1010
1001
1000
1111
Note: Decimal codes are only valid for the ten decimal digits 0 through 9.
2421 code
0000
0001
0010
0011
0100
1011
1100
1101
1110
1111

## Slide 8: 4. BCD to Excess-3 Code Converter (2/3)
Truth table:
 | BCD |  |  |  | Excess-3 |  |  | 
 | A | B | C | D | W | X | Y | Z
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
2 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1
3 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0
4 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1
5 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0
6 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
7 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 0
8 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1
9 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0
10 | 1 | 0 | 1 | 0 | X | X | X | X
11 | 1 | 0 | 1 | 1 | X | X | X | X
12 | 1 | 1 | 0 | 0 | X | X | X | X
13 | 1 | 1 | 0 | 1 | X | X | X | X
14 | 1 | 1 | 1 | 0 | X | X | X | X
15 | 1 | 1 | 1 | 1 | X | X | X | X
K-maps:
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
1
1
1
1
1
W
0
0
0
0
0
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
1
1
1
1
1
X
0
0
0
0
0
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
1
1
1
1
1
Y
0
0
0
0
0
1
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
1
1
1
1
Z
0
0
0
0
0

## Slide 9: 4. BCD to Excess-3 Code Converter (3/3)
1
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
1
1
1
1
Z
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
1
1
1
1
1
W
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
1
1
1
1
1
X
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
1
1
1
1
1
Y
W = A + BC + BD
X = B'C + B'D + BC'D'
Y = C.D + C'.D'
Z = D'
Note: For illustration purpose here, we left out the 0s on the K-map for brevity. In practice, you must fill in all cells.


## Slide 10: 5. Block-Level Design
More complex circuits can also be built using block-level method.
In general, block-level design method (as opposed to gate-level design) relies on algorithms or formulae of the circuit, which are obtained by decomposing the main problem to sub-problems recursively (until small enough to be directly solved by blocks of circuits).
First example shows how to create a 4-bit parallel adder using block-level design.
Using 4-bit parallel adders as building blocks, we can create the following:
  1. BCD-to-Excess-3 Code Converter
  2. 16-bit Parallel Adder

## Slide 11: 5. 4-bit Parallel Adder (1/4)
Consider a circuit to add two 4-bit numbers together and a carry-in, to produce a 5-bit result.
4-bit
Parallel Adder
C5
C1
X2
X1
Y4
Y3
S4
S3
S2
S1
Y2
Y1
X4
X3
Black-box view of 4-bit parallel adder
5-bit result is sufficient because the largest result is: 11112 + 11112 + 12 = 111112

## Slide 12: 5. 4-bit Parallel Adder (2/4)
SSI design (gate-level design) technique should not be used here.
Truth table for 9 inputs is too big: 29 = 512 rows!
Simplification becomes too complicated!
X4X3X2X1 | Y4Y3Y2Y1 | C1 | C5 | S4S3S2S1
0 0 0 0 | 0 0 0 0 | 0 | 0 | 0 0 0 0
0 0 0 0 | 0 0 0 0 | 1 | 0 | 0 0 0 1
0 0 0 0 | 0 0 0 1 | 0 | 0 | 0 0 0 1
… | … | … | … | …
0 1 0 1 | 1 1 0 1 | 1 | 1 | 0 0 1 1
… | … | … | … | …
1 1 1 1 | 1 1 1 1 | 1 | 1 | 1 1 1 1

## Slide 13: 5. 4-bit Parallel Adder (3/4)
Alternative design possible.
Addition formula for each pair of bits (with carry in), Ci+1Si = Xi + Yi + Ci has the same function as a full adder: Ci+1 = Xi Yi + (Xi Yi)Ci Si = Xi  Yi  Ci
C =
X = 1 0 1 0
Y = 1 1 1 1
X + Y =
0
1
1
0
1
1
0
0
1

## Slide 14: 5. 4-bit Parallel Adder (4/4)
Cascading 4 full adders via their carries, we get:
C1
Y1 X1
S1
FA
C2
C5
Y2 X2
S2
FA
C3
Y3 X3
S3
FA
C4
Y4 X4
S4
FA
Output
Input
Note that carry is propagated by cascading the carry from one full adder to the next.
Called Parallel Adder because inputs are presented simultaneously (in parallel). Also called Ripple-Carry Adder.

## Slide 15: 5. 16-bit Parallel Adder
Larger parallel adders can be built from smaller ones.
Example: A 16-bit parallel adder can be constructed from four 4-bit parallel adders:
4-bit // adder
X4..X1
Y4..Y1
C1
S4..S1
4-bit // adder
X8..X5
Y8..Y5
C5
S8..S5
4-bit // adder
X12..X9
Y12..Y9
C9
S12..S9
4-bit // adder
X16..X13
Y16..Y13
C13
S16..S13
C17
4
4
4
4
4
4
4
4
4
4
4
4
A 16-bit parallel adder
4
S4..S1
S4S3S2S1
=

## Slide 16: 5. BCD to Excess-3 Converter: Revisit (1/2)
Excess-3 code can be converted from BCD code using truth table:
 | BCD |  |  |  | Excess-3 |  |  | 
 | A | B | C | D | W | X | Y | Z
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
2 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1
3 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0
4 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1
5 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0
6 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
7 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 0
8 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1
9 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0
10 | 1 | 0 | 1 | 0 | X | X | X | X
11 | 1 | 0 | 1 | 1 | X | X | X | X
12 | 1 | 1 | 0 | 0 | X | X | X | X
13 | 1 | 1 | 0 | 1 | X | X | X | X
14 | 1 | 1 | 1 | 0 | X | X | X | X
15 | 1 | 1 | 1 | 1 | X | X | X | X
Gate-level design can be used since only 4 inputs.
However, alternative design is possible.
Use problem-specific formula:
  Excess-3 code = BCD Code + 00112

## Slide 17: 5. BCD to Excess-3 Converter: Revisit (2/2)
Block-level circuit:
4-bit Parallel Adder
X4
X3
X2
X1
Y4
Y3
Y2
Y1
0
0
1
1
S4
S3
S2
S1
BCD
code
Excess-3
code
unused
0
Cin
Cout
A BCD to Excess-3 Code Converter
Note: In the lab, input 0 (low) is connected to GND, 1 (high) to Vcc.

## Slide 18: 7. Example: 6-Person Voting System
Application: 6-person voting system.
  Use FAs and a 4-bit parallel adder.
  Each FA can sum up to 3 votes.
Voter 1
3-bit Output
A
B
S
Cout
S
Cin
Voter 2
Voter 3
Voter 4
A
B
S
Cout
S
Cin
Voter 5
Voter 6
Full-adder 1
Full-adder 2
S
Cout
Cin
A
1
2
3
4
B
1
2
3
4
S
1
2
3
4
Parallel adder
1
0
1
0
1
0
0
1
1
0
1
1
0
1
1
0
1
1
1
0
1
1
1
1
0
1


## Slide 19: summary
Magnitude Comparator

## Slide 20: 8. Magnitude Comparator (1/4)
Magnitude comparator: compares 2 unsigned values A and B, to check if A>B, A=B, or A<B.
To design an n-bit magnitude comparator using classical method, it would require 22n rows in truth table!
We shall exploit regularity in our design.
Question: How do we compare two 4-bit unsigned values A (a3a2a1a0) and B (b3b2b1b0)?
  If (a3 > b3) then A > B
  If (a3 < b3) then A < B
  If (a3 = b3) then if (a2 > b2) …

## Slide 21: 8. Magnitude Comparator (2/4)
Let A = A3A2A1A0 , B = B3B2B1B0; xi = AiBi + Ai'Bi'
A2
B2
A3
B3
A0
B0
A1
B1
(A < B)
(A > B)
(A = B)
x3
x2
x1
x0
A3'B3
A3B3'
A3'B3 + x3A2'B2
+ x3x2.A1'B1
+ x3x2x1A0'B0
A3B3' + x3A2B2'
+ x3x2A1B1'
+ x3x2x1A0B0'
x3x2x1x0


## Slide 22: 8. Magnitude Comparator (4/4)
A function F accepts a 4-bit binary value ABCD, and returns 1 if 3  ABCD  12, or 0 otherwise. How would you implement F using magnitude comparators and a suitable logic gate?
A3
A2
A1
A0
4-bit Comp
(A < B)
(A > B)
(A = B)
B3
B2
B1
B0
A3
A2
A1
A0
4-bit Comp
(A < B)
(A > B)
(A = B)
B3
B2
B1
B0
A3
A2
A1
A0
4-bit Comp
(A < B)
(A > B)
(A = B)
B3
B2
B1
B0
A3
A2
A1
A0
4-bit Comp
(A < B)
(A > B)
(A = B)
B3
B2
B1
B0
A
B
C
D
0
0
1
0
1
1
0
1
F


## Slide 23: summary
Circuit Delays

## Slide 24: 9. Circuit Delays (1/5)
Given a logic gate with delay t. If inputs are stable at times t1, t2, …, tn, then the earliest time in which the output will be stable is: max( t1, t2, …, tn ) + t
t1
Logic
Gate
t2
tn
:
:
max (t1, t2, ..., tn ) + t
To calculate the delays of all outputs of a combinational circuit, repeat above rule for all gates.

## Slide 25: 9. Circuit Delays (2/5)
As a simple example, consider the full adder circuit where all inputs are available at time 0. Assume each gate has delay t.
Outputs S and C experience delays of 2t and 3t respectively.
max(0,0)+t = t
t
X
Y
S
C
Z
0
0
0
max(t,0)+t = 2t
max(t,2t)+t = 3t
2t

## Slide 26: 9. Circuit Delays (3/5)
More complex example: 4-bit parallel adder.
C1
Y1 X1
S1
FA
C2
C5
Y2 X2
S2
FA
C3
Y3 X3
S3
FA
C4
Y4 X4
S4
FA
0
0
0
0
0
0
0
0
0

## Slide 27: 9. Circuit Delays (4/5)
Analyse the delay for the repeated block.
where Xi, Yi are stable at 0t, while Ci is assumed to be stable at mt.
Full
Adder
Xi
Yi
Ci
Si
Ci+1
0
0
mt
Performing the delay calculation:
Xi
Yi
Si
Ci+1
Ci
max(0,0)+t = t
t
0
0
mt
max(t,mt)+t
max(t,mt)+2t
max(t,mt)+t

## Slide 28: 9. Circuit Delays (5/5)
Calculating:
  When i=1, m=0; S1 = 2t and C2 = 3t
  When i=2, m=3; S2 = 4t and C3 = 5t
  When i=3, m=5; S3 = 6t and C4 = 7t
  When i=4, m=7; S4 = 8t and C5 = 9t
In general, an n-bit ripple-carry parallel adder will experience the following delay times:
  Sn = ( (n – 1)2 + 2 ) t
  Cn+1 = ( (n – 1)2 + 3 ) t
Propagation delay of ripple-carry parallel adders is proportional to the number of bits it handles.
Maximum delay: ( (n – 1)2 + 3 ) t
Full
Adder
Xi
Yi
Ci
Si
Ci+1
0
0
mt
max(t,mt)+t
max(t,mt)+2t

## Slide 29: quizzes
19. Combinational Circuits Quiz 1
20. Combinational Circuits Quiz 2

## Slide 30: 19. Combinational Circuits Quiz 1 Q1


## Slide 31: 20. Combinational Circuits Quiz 2 Q1
w=ab
x=b+c
c'
  F = w  x
  = w'x + wx'
  = (a.b)'(b+c) + (a.b)(b+c)'
  = (a'+b').(b+c) + (a.b).(b'.c')
  = a'.b + a'.c + b'.b + b'.c + a.b.b'.c'
  = a'.b + a'.c + 0 + b'.c + 0
  = a'.b + a'.c + b'.c
  = a'.b + b'.c
Concensus Theorem:
XY + X'Z + YZ = XY + X'Z


## Slide 32: 20. Combinational Circuits Quiz 2 Q2, Q3
1ns
2ns
2ns
3ns
2ns
5ns
4ns


## Slide 33: Past YEARs’ QUESTIONS
Combinational Circuits

## Slide 34
Past years’ exam questions
AY2020/21 Sem2 Q13(d)
AY2021/22 Sem1 Q13(a)
AY2021/22 Sem2 Q14(b)(c)
AY2023/24 Sem1 Q17(a)(b)(d)
Assumption
Logical constants 0 and 1 are available, but not complemented literals.

## Slide 35: AY2020/21 Sem2 Q13(d)

## Slide 36: AY2020/21 Sem2 Q13(d)
When y=0: Z3Z2Z1Z0 = X2X1X0 + 000
When y=1: Z3Z2Z1Z0 = X2X1X0 + 101
Z = X + 5y


## Slide 37: AY2021/22 Sem1 Q13(a)
A | B | C | D | E | F | G | H
0 | 0 | 0 | 0 |  |  |  | 
0 | 0 | 0 | 1 |  |  |  | 
0 | 0 | 1 | 0 |  |  |  | 
0 | 0 | 1 | 1 |  |  |  | 
0 | 1 | 0 | 0 |  |  |  | 
0 | 1 | 0 | 1 |  |  |  | 
0 | 1 | 1 | 0 |  |  |  | 
0 | 1 | 1 | 1 |  |  |  | 
1 | 0 | 0 | 0 |  |  |  | 
1 | 0 | 0 | 1 |  |  |  | 
1 | 0 | 1 | 0 |  |  |  | 
1 | 0 | 1 | 1 |  |  |  | 
1 | 1 | 0 | 0 |  |  |  | 
1 | 1 | 0 | 1 |  |  |  | 
1 | 1 | 1 | 0 |  |  |  | 
1 | 1 | 1 | 1 |  |  |  | 
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
0
0
0
0
1
1
1
1
1
1
1
1
0
0
0
0
0
0
1
1
1
1
0
0
0
0
1
1
1
1
0
0
0
1
1
0
0
1
1
0
0
1
1
0
0
1
1
0
E(A,B,C,D) = m(8,9,10,11,12,13,14,15)
F(A,B,C,D) = m(4,5,6,7,8,9,10,11)
G(A,B,C,D) = m(2,3,4,5,10,11,12,13)
H(A,B,C,D) = m(1,2,5,6,9,10,13,14)


## Slide 38: AY2021/22 Sem2 Q14(b)
Part (a) answer: F = m(0, 5, 10, 15)
A | B | C | D | F
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1
What is this circuit?
It is a 2-bit adder-cum-substractor. If Cin is set to 0, it performs X + Y.
If Cin is 1, it performs X – Y.
Since F=1 when AB=CD, or AB – CD = 0, the solution is…
1
A
B
C
D
F


## Slide 39: AY2021/22 Sem2 Q14(c)
D
B
A
C
G
1
0
0
0
1
0
0
1
1
1
1
1
1
1
0
1
5 PIs
5 EPIs
G = A·B + C'·D' + A·C' + B·D' + A·D'
A | B | C | D | G
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
Observation: G = (AB ≥ DC)
(Other answers possible. Eg: ABC DCB, ABCD DCBA).
0
0
A
B
0
0
D
C
G


## Slide 40: AY2023/24 Sem1 Q17(a)
Z
X
W
Y
P
d
1
0
d
0
d
0
0
0
1
d
0
1
d
0
d
4 PIs: Y'Z, X’Y’, X’Z’, WXZ
0 EPI


## Slide 41: AY2023/24 Sem1 Q17(b)
Z
X
W
Y
Q
d
1
d
d
d
0
0
1
1
0
0
d
0
d
1
0
4 PIs: W'X’, W’Z’, X’Z, XZ’
2 EPIs: X’Z, XZ’


## Slide 42: AY2023/24 Sem1 Q17(d)
A | B | C | D | R
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1
R(A,B,C,D) = m(0,3,12,15).


## Slide 43
Reminder
Assignment 2
Due 16 March 2026, Monday (Today!) 1pm
Logic Trainer Lab
Attend to learn how to use the logic trainer for subsequent labs!

## Slide 44: Next Week
MSI Components:
Decoders, Encoders, Multiplexers, Demultiplexers
Past years’ exam questions:
AY2016/17 Sem2 Q2
AY2017/18 Sem2 Q3(a)(b)(c)
AY2018/19 Sem2 Q5(c)
AY2019/20 Sem2 Q5(a)(b)

## Slide 45: End of File