## Slide 1: https://www.comp.nus.edu.sg/~cs2100/
CS2100 Recitation 9
MSI Components
23 March 2026
Aaron Tan

## Slide 2: Contents
Decoders
  Implementing functions using decoders
  Decoder with enable
  Standard MSI decoder
Encoders
  Priority encoders
Multiplexers
  Standard MSI multiplexer
  Implementing functions using multiplexers
  Using smaller multiplexers
Selected Past Years’ Exam Questions
AY2016/17 Sem2 Q2
AY2017/18 Sem2 Q3(a)(b)(c)
AY2018/19 Sem2 Q5(c)
AY2019/20 Sem2 Q5(a)(b)

## Slide 3: summary
Decoders
decoder
code
entity

## Slide 4: Decoding – the inefficient way
0
1
2
3
4
5
6
7
0
0
0
0
0
1
0
0

## Slide 5: Decoding – the better way
1
0
1
0
1
2
3
4
5
6
7
Some device

## Slide 6: 2. Decoders (2/5)
Example: If codes 00, 01, 10, 11 are used to identify four persons, we may use a 2-bit decoder.
2x4
DEC
2-bit code
X
Y
F0 F1 F2 F3
Person 0
Person 1
Person 2
Person 3
This is a 24 decoder which selects an output line based on the 2-bit code supplied.
Truth table:
X | Y | F0 | F1 | F2 | F3
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1

## Slide 7: 2. Decoders (3/5)
From truth table, circuit for 24 decoder is:
F0 = X'Y'
F1 = X'Y
F2 = XY'
F3 = XY
X
Y
Each output is a minterm (X'Y', X'Y, XY' or XY) of a 2-variable function.
X | Y | F0 | F1 | F2 | F3
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1

## Slide 8: 2. Decoders (4/5)
Design a 38 decoder.
F1 = x'y'z
x
z
y
F0 = x'y'z'
F2 = x'yz'
F3 = x'yz
F5 = xy'z
F4 = xy'z'
F6 = xyz'
F7 = xyz
x | y | z | F0 | F1 | F2 | F3 | F4 | F5 | F6 | F7
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
Each output is a minterm of a 3-variable function.

## Slide 9: 2. Decoders: Implementing Functions (1/3)
A Boolean function, in sum-of-minterms form a
  decoder to generate the minterms, and
  an OR gate to form the sum.
Any combinational circuit with n inputs and m outputs can be implemented with an n:2n decoder with m OR gates.
Good when circuit has many outputs, and each function is expressed with a few minterms.

## Slide 10: 2. Decoders: Implementing Functions (2/3)
Example: Full adder
  S(x, y, z) = S m(1,2,4,7)
  C(x, y, z) = S m(3,5,6,7)
3x8
DEC
S2
S1
S0
x
y
z
0
1
2
3
4
5
6
7
S
C

## Slide 11: 2. Decoders: Implementing Functions (3/3)

3x8
DEC
S2
S1
S0
x
y
z
0
1
2
3
4
5
6
7
S
C
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
1
0
0
0
0
0
0
1
0
1
1
1
0
0
0
0
0
0
0
1
1
1
BRAVO!!!
  S(x, y, z) = S m(1,2,4,7)
  C(x, y, z) = S m(3,5,6,7)

## Slide 12: 2. Decoders with Enable (1/2)
Decoders often come with an enable control signal, so that the device is only activated when the enable, E = 1.
Truth table:
Circuit of a 24 decoder with enable:
X
Y
F0 = EX'Y'
F1 = EX'Y
F2 = EXY'
F3 = EXY
E
E | X | Y | F0 | F1 | F2 | F3
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 1
0 | d | d | 0 | 0 | 0 | 0

## Slide 13: 2. Decoders with Enable (2/2)
In the previous slide, the decoder has a one-enable control signal, i.e. the decoder is enabled with E=1.
In most MSI decoders, enable signal is zero-enable, usually denoted by E' or Ē. The decoder is enabled when the signal is zero (low).
Decoder with 1-enable
Decoder with 0-enable
E | X | Y | F0 | F1 | F2 | F3
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 1
0 | d | d | 0 | 0 | 0 | 0
E' | X | Y | F0 | F1 | F2 | F3
0 | 0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1
1 | d | d | 0 | 0 | 0 | 0

## Slide 14: 2. Constructing Larger Decoders (1/4)
Larger decoders can be constructed from smaller ones.
Example: A 38 decoder can be built from two 24 decoders (with one-enable) and an inverter.
3x8
DEC
S2
S1
S0
w
x
y
0
1
:
:
7
F0 = w'x'y'
F1 = w'x'y
:
:
F7 = wxy
2x4
DEC
S1
S0
0
1
2
3
F0 = w'x'y'
F1 = w'x'y
F2 = w'xy'
F3 = w'xy
E
2x4
DEC
S1
S0
0
1
2
3
F4 = wx'y'
F5 = wx'y
F6 = wxy'
F7 = wxy
E
w
x
y

## Slide 15: 2. Constructing Larger Decoders (2/4)

0
1
2
3
2x4
Dec
S1
S0
0
1
2
3
F0 = w'x'y'
F1 = w'x'y
F2 = w'xy'
F3 = w'xy
E
2x4
Dec
S1
S0
F4 = wx'y'
F5 = wx'y
F6 = wxy'
F7 = wxy
E
w
x
y
3x8
Dec
S2
S1
S0
w
x
y
0
1
:
:
7
F0 = w'x'y'
F1 = w'x'y
:
:
F7 = wxy
0
0
0
0
0
0
0
1
0
0
0
1
0
0
0
1
1
0
0
0
0
0
0
1
0
0
1
1
0
0
1
0
0
1
0
0
0
0
0
BRAVO!!!

## Slide 16: 2. Constructing Larger Decoders (3/4)
Construct a 416 decoder from two 38 decoders with one-enable and an inverter.
4x16
DEC
S3
S2
S1
S0
w
x
y
z
0
1
:
:
15
F0
F1
:
:
F15
3x8
DEC
S2
S1
S0
0
1
:
7
F0
F1
:
F7
E
3x8
DEC
S2
S1
S0
0
1
:
7
F8
F9
:
F15
E
w
x
y
z
Note: The input w and its complement w' are used to select either one of the two smaller decoders.

## Slide 17
Exercise: How to construct a 416 decoder using five 24 decoders with enable?
2x4
Dec
S1
S0
0
1
2
3
E
F0 = (w'x')y'z'
F1 = (w'x')y'z
F2 = (w'x')yz'
F3 = (w'x')yz
y
z
2x4
Dec
S1
S0
0
1
2
3
E
w
x
1
2x4
Dec
S1
S0
0
1
2
3
E
F4 = (w'x)y'z'
F5 = (w'x)y'z
F6 = (w'x)yz'
F7 = (w'x)yz
y
z
2x4
Dec
S1
S0
0
1
2
3
E
F8 = (wx')y'z'
F9 = (wx')y'z
F10 = (wx')yz'
F11 = (wx')yz
y
z
2x4
Dec
S1
S0
0
1
2
3
E
F12 = (wx)y'z'
F13 = (wx)y'z
F14 = (wx)yz'
F15 = (wx)yz
y
z

## Slide 18: Negated outputs (active low outputs) decoders
A decoder may be 1-enabled or 0-enabled.
A decoder may also normal output or negated outputs. (See next two slides.)
  Normal outputs = active high outputs
  Negated outputs = active low outputs
E | X | Y | F0 | F1 | F2 | F3
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 1
0 | d | d | 0 | 0 | 0 | 0
1-enabled, active high outputs 2x4 decoder.
1-enabled, active low outputs 2x4 decoder.
E | X | Y | F0 | F1 | F2 | F3
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 0
0 | d | d | 1 | 1 | 1 | 1

## Slide 19: 2. Standard MSI Decoder (1/2)
74138 (3-to-8 decoder)
74138 decoder module.
(a) Logic circuit.
(b) Package pin configuration.

## Slide 20: 2. Standard MSI Decoder (2/2)
74138 decoder module.
(d) Generic symbol.
(e) IEEE standard logic symbol.
Source:The Data Book Volume 2, Texas Instruments Inc.,1985
74138 decoder module.
(c) Function table.
(c)

## Slide 21: 2. Decoders: Implementing Functions Revisit (1/2)
Example: Implement the following function using a 38 decoder and an appropriate logic gate
  f(Q,X,P) =  m(0,1,4,6,7) =  M(2,3,5)
We may implement the function in several ways:
  Using a decoder with active-high outputs with an OR gate: f(Q,X,P) = m0 + m1 + m4 + m6 + m7
  Using a decoder with active-low outputs with a NAND gate: f(Q,X,P) = (m0'  m1'  m4'  m6'  m7' )'
  Using a decoder with active-high outputs with a NOR gate: f(Q,X,P) = (m2 + m3 + m5 )' [ = M2  M3  M5 ]
  Using a decoder with active-low outputs with an AND gate: f(Q,X,P) = m2'  m3'  m5'

## Slide 22: 2. Decoders: Implementing Functions Revisit (2/2)
f(Q,X,P) = Sm(0,1,4,6,7) =  M(2,3,5)
3x8
Dec
A
B
C
Q
X
P
0
1
2
3
4
5
6
7
f(Q,X,P)
(a) Active-high decoder with OR gate.
f(Q,X,P)
3x8
Dec
A
B
C
Q
X
P
0
1
2
3
4
5
6
7
(b) Active-low decoder with NAND gate.
3x8
Dec
A
B
C
Q
X
P
0
1
2
3
4
5
6
7
f(Q,X,P)
(c) Active-high decoder with NOR gate.
f(Q,X,P)
3x8
Dec
A
B
C
Q
X
P
0
1
2
3
4
5
6
7
(d) Active-low decoder with AND gate.
(m0'·m1'·m4'·m6'·m7)'
=m0+m1+m4+m6+m7
(m2+m3+m5)'
= m2'·m3'·m5'
= M2·M3·M5
m2'·m3'·m5'
= M2·M3·M5

## Slide 23: summary
Encoders
encoder
code
entity

## Slide 24: 3. Encoders (1/4)
Encoding is the converse of decoding.
Given a set of input lines, of which exactly one is high and the rest are low, the encoder provides a code that corresponds to that high input line.
Contains 2n (or fewer) input lines and n output lines.
Implemented with OR gates.
Example:
4-to-2 Encoder
F0
F1
F2
F3
D0
D1
Select via switches
2-bits code

## Slide 25: Encoding – the inefficient way
0
1
2
3
4
5
6
7
0
0
0
0
0
1
0
0

## Slide 26: Encoding – the better way
0
1
2
3
4
5
6
7
1
0
1
Some device

## Slide 27: 3. Encoders (2/4)
Truth table:

With K-map, we obtain:
  D1 = F2 + F3
  D0 = F1 + F3
F0
F1
F2
F3
D1
D0
Simple 4-to-2 encoder
X | 1 | X | 1
0 | X | X | X
X | X | X | X
0 | X | X | X
F1
F2
F3
F0
D1
X | 1 | X | 0
1 | X | X | X
X | X | X | X
0 | X | X | X
F1
F2
F3
F0
D0
Circuit:

## Slide 28: 3. Encoders (3/4)
Example: 8-to-3 encoder.
  At any one time, only one input line of an encoder has a value of 1 (high), the rest are zeroes (low).

## Slide 29: 3. Encoders (4/4)
Example: 8-to-3 encoder.
An 8-to-3 encoder
D0
D1
D2
D3
D4
D5
D6
D7
z = D1 + D3 + D5 + D7
y = D2 + D3 + D6 + D7
x = D4 + D5 + D6 + D7
Exercise: Can you design a 2n-to-n encoder without using K-map?

## Slide 30: 3. Priority Encoders (1/2)
A priority encoder is one with priority
  To allow for more than one input line to carry a 1.
  If two or more inputs or equal to 1, the input with the highest priority takes precedence.
  If all inputs are 0, this input combination is considered invalid.
Example of a 4-to-2 priority encoder:
Inputs |  |  |  | Outputs |  | 
D0 | D1 | D2 | D3 | f | g | V
0 | 0 | 0 | 0 | X | X | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
X | 1 | 0 | 0 | 0 | 1 | 1
X | X | 1 | 0 | 1 | 0 | 1
X | X | X | 1 | 1 | 1 | 1

## Slide 31: 3. Priority Encoders (2/2)
Understanding “compact” function table
Inputs |  |  |  | Outputs |  | 
D0 | D1 | D2 | D3 | f | g | V
0 | 0 | 0 | 0 | X | X | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
X | 1 | 0 | 0 | 0 | 1 | 1
X | X | 1 | 0 | 1 | 0 | 1
X | X | X | 1 | 1 | 1 | 1
Inputs |  |  |  | Outputs |  | 
D0 | D1 | D2 | D3 | f | g | V
0 | 0 | 0 | 0 | X | X | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 0 | 1 | 1
1 | 1 | 0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 0 | 1 | 0 | 1
0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 0 | 1 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
Exercise: Obtain the simplified expressions for f, g and V.


## Slide 32
Inputs |  |  |  | Outputs |  | 
D0 | D1 | D2 | D3 | f | g | V
0 | 0 | 0 | 0 | X | X | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 0 | 1 | 1
1 | 1 | 0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 0 | 1 | 0 | 1
0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 0 | 1 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
Exercise: Obtain the simplified expressions for f, g and V.
Hi Prof, please go through priority encoder and how to map out the expression using kmap. Slide 34 lect 18.
X | 1 | 1 | 1
0 | 1 | 1 | 1
0 | 1 | 1 | 1
0 | 1 | 1 | 1
D1
D2
D3
D0
f
X | 1 | 1 | 0
1 | 1 | 1 | 0
1 | 1 | 1 | 0
0 | 1 | 1 | 0
D1
D2
D3
D0
g
0 | 1 | 1 | 1
1 | 1 | 1 | 1
1 | 1 | 1 | 1
1 | 1 | 1 | 1
D1
D2
D3
D0
V

## Slide 33: summary
Multiplexers
mux
data
input
select

## Slide 34
0
1
0
1
0
1
1
0

## Slide 35: Multiplexers and Demultiplexers
An application:
Helps share a single communication line among a number of devices.
At any time, only one source and one destination can use the communication line.

## Slide 36: 5. Multiplexers (1/4)
A multiplexer is a device that has
  A number of input lines
  A number of selection lines
  One output line
It steers one of 2n inputs to a single output line, using n selection lines. Also known as a data selector.
2n:1
Multiplexer
output
inputs
:
select
...

## Slide 37: 5. Multiplexers (2/4)
Truth table for a 4-to-1 multiplexer:
4:1mux
Y
Inputs
select
S1 S0
I0
I1
I2
I3
4:1
MUX
Y
Inputs
select
S1 S0
I0
I1
I2
I3
0
1
2
3
Output

## Slide 38: 5. Multiplexers (3/4)
Output of multiplexer is
  “sum of the (product of data lines and selection lines)”
Example: Output of a 4-to-1 multiplexer is:
  Y = ?
I0∙(S1'∙S0') + I1∙(S1'∙S0) + I2∙(S1∙S0') + I3∙(S1∙S0)
Note:
Expressing
I0∙(S1'∙S0') + I1∙(S1'∙S0) + I2∙(S1∙S0') + I3∙(S1∙S0)
in minterms notation, it is equal to
I0∙m0 + I1∙m1 + I2∙m2 + I3∙m3
This is useful later (eg: slide 45).

## Slide 39: 5. Multiplexers (4/4)
A 4:1 multiplexer circuit:
S1
S0
0 1 2 3
2-to-4 Decoder
I0
I1
I2
I3
Y
S1
S0
I0
I1
I2
I3
Y
A 2n-to-1-line multiplexer, or simply 2n:1 MUX, is made from an n:2n decoder by adding to it 2n input lines, one to each AND gate.

## Slide 40: 5. Multiplexer IC Package
Some IC packages have a few multiplexers in each package (chip). The selection and enable inputs are common to all multiplexers within the package.
S
(select)
A0
A1
A2
A3
B0
B1
B2
B3
E'
(enable)
Y0
Y1
Y2
Y3
Quadruple 2:1 multiplexer

## Slide 41: 5. Standard MSI Multiplexer (1/2)
74151A 8-to-1 multiplexer. (a) Package configuration. (b) Function table.
(b)

## Slide 42: 5. Standard MSI Multiplexer (2/2)
74151A 8-to-1 multiplexer. (c) Logic diagram. (d) Generic logic symbol. (e) IEEE standard logic symbol.
Source: The TTL Data Book Volume 2. Texas Instruments Inc.,1985.
(c)

## Slide 43: 5. Multiplexers: Implementing Functions (1/3)
Boolean functions can be implemented using multiplexers.
A 2n-to-1 multiplexer can implement a Boolean function of n input variables, as follows:
  1. Express in sum-of-minterms form.
  Example: F(A,B,C) = A'B'C + A'BC + AB'C + ABC' = S m(1,3,5,6)
  2. Connect n variables to the n selection lines.
  3. Put a ‘1’ on a data line if it is a minterm of the function, or ‘0’ otherwise.

## Slide 44: 5. Multiplexers: Implementing Functions (2/3)
F(A,B,C) = S m(1,3,5,6)
mux
A B C
0
1
2
3
4
5
6
7
0
1
0
1
0
1
1
0
F
This method works because:
Output = I0m0 + I1m1 + I2m2 + I3m3 + I4m4 + I5m5 + I6m6 + I7m7
Supplying ‘1’ to I1,I3,I5,I6 , and ‘0’ to the rest:
Output = m1 + m3 + m5 + m6
From slide 34 (4:1 mux)
Expressing
I0∙(S1'∙S0') + I1∙(S1'∙S0) + I2∙(S1∙S0') + I3∙(S1∙S0)
in minterms notation, it is equal to
I0∙m0 + I1∙m1 + I2∙m2 + I3∙m3

## Slide 45: 5. Multiplexers: Implementing Functions (3/3)
Example: Use a 74151A to implement f(x1,x2,x3) = S m(0,2,3,5)
Realization of f(x1,x2,x3) = m(0,2,3,5).
(a) Truth table.
(b) Implementation with 74151A.

## Slide 46: 5. Using Smaller Multiplexers (1/6)
Earlier, we saw how a 2n-to-1 multiplexer can be used to implement a Boolean function of n (input) variables.
However, we can use a single smaller 2(n-1)-to-1 multiplexer to implement a Boolean function of n (input) variables.
Example: The function F(A,B,C) = S m(1,3,5,6) can be implemented using a 4-to-1 multiplexer (rather than an 8-to-1 multiplexer).

## Slide 47: 5. Using Smaller Multiplexers (2/6)
Let’s look at this example:
  F(A,B,C) = S m(0,1,3,6) = A'B'C' + A'B'C + A'BC + ABC'
mux
A B C
0
1
2
3
4
5
6
7
1
1
0
1
0
0
1
0
F
mux
A B
0
1
2
3
1
C
0
C'
F
Note: Two of the variables, A and B, are applied as selection lines of the multiplexer, while the inputs of the multiplexer contain 1, C, 0 and C'.

## Slide 48: 5. Using Smaller Multiplexers (3/6)
Procedure
  1. Express Boolean function in sum-of-minterms form. Example: F(A,B,C) = S m(0,1,3,6)
  2. Reserve one variable (in our example, we take the least significant one) for input lines of multiplexer, and use the rest for selection lines. Example: C is for input lines; A and B for selection lines.

## Slide 49: 5. Using Smaller Multiplexers (4/6)
  3. Draw the truth table for function, by grouping inputs by selection line values, then determine multiplexer inputs by comparing input line (C) and function (F) for corresponding selection line values.
mux
A B
0
1
2
3
1
0
F
C
A | B | C | F | MUX input
0 | 0 | 0 | 1 | 
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 0 | 
0 | 1 | 1 | 1 | 
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | 0 | 
1
C
0
C'


## Slide 50: 5. Using Smaller Multiplexers (5/6)
Alternative: What if we use A for input lines, and B, C for selector lines?
A' (when BC = 00)
A' (when BC = 01)
A (when BC = 10)
A' (when BC = 11)
mux
B C
0
1
2
3
A
F
mux
B C
0
1
2
3
?
?
?
?
F


## Slide 51: 5. Using Smaller Multiplexers (6/6)
Example: Implement the function below with 74151A:
  f(x1,x2,x3,x4) = S m(0,1,2,3,4,9,13,14,15)

## Slide 52: Peeking Ahead
1K x 8
DATA (8)
ADRS (10)
CS
RW
Read/write
(8)
Output data
1K x 8
DATA (8)
ADRS (10)
CS
RW
(8)
1K x 8
DATA (8)
ADRS (10)
CS
RW
(8)
1K x 8
DATA (8)
ADRS (10)
CS
RW
(8)
0–1023
1024 – 2047
2048 – 3071
3072 – 4095
Input data
8 lines
0
1
2
3
2x4 decoder
Lines
Lines
0 – 9
11 10
S0
S1
Address
1K x 8
DATA (8)
ADRS (10)
CS
RW
(8)
Output data
8 lines
Input data
8 lines
Enable
Read/write
Address
10 lines
1K x 8bits RAM
Building a 4K x 8bits RAM using 1K x 8bits RAMs.
4K locations 12-bit address.

## Slide 53: QnA Queries (Past Semester’s)

## Slide 54
For tutorial 7 q1 why is the 2nd input 0 and E why it cannot be D and E?
0
0
0
1
0
D
2-bit
Adder
Cin
X1
X0
Y1
Y0
Cout
S1
S0
Full
Adder
X
Y
Z
Carry
Sum
4-bit
COMP
X3
X2
X1
X0
Y3
Y2
Y1
Y0
X<Y
X=Y
X>Y
A
B
C
0
E
V

## Slide 55
A | B | C | D | E | F | G | H
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 0 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 0 | 0 | 0
EFGH = (ABCD+1)/2
Cin
Cin
X3
X2
X1
X0
Y3
Y2
Y1
Y0
4-bit
// adder
Cout
S3
S2
S1
S0
Q2(a)
Can you go through tutorial 7 q2?
0
A
B
C
0
0
0
D
0
E
F
G
H

## Slide 56
A | B | C | D | E | F | G | H
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 0 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 0 | 0 | 0
EFGH = (ABCD+1)/2
Cin
Cin
X3
X2
X1
X0
Y3
Y2
Y1
Y0
4-bit
// adder
Cout
S3
S2
S1
S0
Q2(a)
A
B
C
D
0
0
0
0
1
E
F
G
H
Can you go through tutorial 7 q2?

## Slide 57
P | Q | R | S | W | X | Y | Z
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
A1H
Cin
A
B
C
D
E
F
G
H
4221-to-8421 decimal code converter
57
Q2(b)
S
Z
0
P
Q
R
0
W
X
Y
Can you go through tutorial 7 q2?

## Slide 58: Past YEARs’ QUESTIONS
MSI Components

## Slide 59
Past years’ exam questions
AY2016/17 Sem2 Q2
AY2017/18 Sem2 Q3(a)(b)(c)
AY2018/19 Sem2 Q5(c)
AY2019/20 Sem2 Q5(a)(b)
Assumption
Logical constants 0 and 1 are available, but not complemented literals.

## Slide 60: AY2016/17 Sem2 Q2(a)
A | B | C | D | F
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0
2-bit
COMP
X<Y
X=Y
X>Y
X
1
0
Y
1
0
A
C
B
D
F
F = AC < BD
Other answers possible.
Observe that


## Slide 61: AY2016/17 Sem2 Q2(b)
0
1
2
3
2×4
DEC
S1
S0
EN
Observe that
G(A,B,C,D) = m(2, 11)
= A'B'CD' + AB'CD
= C((A'D' + AD) B')
= C((A  D)' B')
C
A  D
B
G


## Slide 62: AY2017/18 Sem2 Q3(a)
A | B | F
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
0
0
1
1
F = A


## Slide 63: AY2017/18 Sem2 Q3(b)
G
0
0
1
2
3
4
5
6
7
1
2
8:1
MUX
A | B | C | D | F
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
A C D
1
B
0
1
B
0
1
B


## Slide 64: AY2017/18 Sem2 Q3(c)
24
DEC
EN
S1
S0
0
1
2
3
Other alternative answers possible.
A
B
C
H
H(A,B,C,D) = m(12, 13)
= ABC'D' + ABC'D
= A(BC'D' + BC'D)
= A(BC')


## Slide 65: AY2018/19 Sem2 Q5(c)
010 = 0000 00002
1710 = 0001 00012
3410 = 0010 00102
5110 = 0011 00112
6810 = 0100 01002
8510 = 0101 01012
:
25510 = 1111 11112
A
B
C
D
E
F
G
H
COMP
X
X < Y
X = Y
X > Y
3
2
1
0
3
2
1
0
Y
Q


## Slide 66: AY2019/20 Sem2 Q5(a)
A | B | C | N
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
N = A + B + C
E + (S1’  S0’)’
E + (S1’  S0)’
E + (S1  S0’)’
E + (S1  S0)’
C
A
B
N


## Slide 67: AY2019/20 Sem2 Q5(b)
AB | CD | AB<CD | AB>CD | (MUX) S1S0 | (DEMUX) S1S0 | PQRS | PQRS
00 | 00 | 0 | 0 | 00 | 00 | A000 | 0000
00 | 01 | 1 | 0 | 10 | 01 | 0C00 | 0000
00 | 10 | 1 | 0 | 10 | 01 | 0C00 | 0100
00 | 11 | 1 | 0 | 10 | 01 | 0C00 | 0100
01 | 00 | 0 | 1 | 01 | 10 | 00B0 | 0010
01 | 01 | 0 | 0 | 00 | 00 | A000 | 0000
01 | 10 | 1 | 0 | 10 | 01 | 0C00 | 0100
01 | 11 | 1 | 0 | 10 | 01 | 0C00 | 0100
10 | 00 | 0 | 1 | 01 | 10 | 00B0 | 0000
10 | 01 | 0 | 1 | 01 | 10 | 00B0 | 0000
10 | 10 | 0 | 0 | 00 | 00 | A000 | 1000
10 | 11 | 1 | 0 | 10 | 01 | 0C00 | 0100
11 | 00 | 0 | 1 | 01 | 10 | 00B0 | 0010
11 | 01 | 0 | 1 | 01 | 10 | 00B0 | 0010
11 | 10 | 0 | 1 | 01 | 10 | 00B0 | 0010
11 | 11 | 0 | 0 | 00 | 00 | A000 | 1000
P = A∙B∙C∙D + A∙B'∙C∙D'
Q = A'∙C + B'∙C∙D
R = B∙C'∙D'+ A∙B∙C'+ A∙B∙D'


## Slide 68: quiz
21. MSI Components Quiz

## Slide 69: Question 1
A | B | C | D | F
0 | 0 | 0 | 0 | 
0 | 0 | 0 | 1 | 
0 | 0 | 1 | 0 | 
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 0 | 
0 | 1 | 0 | 1 | 
0 | 1 | 1 | 0 | 
0 | 1 | 1 | 1 | 
1 | 0 | 0 | 0 | 
1 | 0 | 0 | 1 | 
1 | 0 | 1 | 0 | 
1 | 0 | 1 | 1 | 
1 | 1 | 0 | 0 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | 0 | 
1 | 1 | 1 | 1 | 
0
0
0
0
0
0
0
0
0
1
0
0
0
0
1
1
B.A'.C'.D = m5
B.A.C.D' = m14
B.A.C.D = m15


## Slide 70: Question 2
A | B | C | G
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
BC = 00
BC = 01
BC = 10
BC = 11
0
0
0
1
1
0
1
1


## Slide 71: Next Week
Sequential Circuits
Past years’ exam questions:
AY2015/16 Sem1 Q7
AY2020/21 Sem2 Q12

## Slide 72: End of File