## Slide 1: Rate Adaptations

## Slide 2
You are Here
Network
Encoder
Sender
Middlebox
Receiver
Decoder

## Slide 3: Sender’s Algorithm
open UDP socket
foreach video frame
chop into packets
add RTP header
send to network

## Slide 4: Sender’s Algorithm
open UDP socket
foreach video frame
chop into packets
add RTP header
send to network
wait for 1/fps seconds

## Slide 5: Sender’s Algorithm
open UDP socket
foreach video frame
chop into packets
add RTP header
send to network
wait for 1/fps seconds
Send frames at equal time distance.

## Slide 6: Sender’s Algorithm
open UDP socket
foreach video frame
chop into packets
foreach packet
add RTP header
send to network
wait for size/bps seconds
Send data at constant bandwidth.

## Slide 7: Rules
Transmission rate should match encoding rate
Transmission should not be too bursty

## Slide 8: Two Approaches
Just send at a fix rate
  or “I hope the network can handle it” approach

## Slide 9: Effects on TCP: Simulation
From Sisalem, Emanuel and Schulzrinne paper on
“Direct Adjustment Algorithm.”

## Slide 10: Effects on TCP

## Slide 11: DAA Parameters
Adaptive RTP flows
  Additive increase/multiplicative decrease
    50 kb and factor 0.875
  RTCP: min 5 sec inter-report time
  Loss thresholds: 5% and 10%
TCP
  Immediate loss notification
  Transmission window is halved

## Slide 12: Demo
Effects of UDP on TCP without congestion control

## Slide 13: Two Approaches
Just send at a fixed rate
  or “I hope the network can handle it” approach
Adapt transmission/encoding rate to network condition

## Slide 14: How to Adapt?
if network condition is bad
reduce rate
else if network condition is so-so
do nothing
else if network condition is good
increase rate

## Slide 15: How to ..
Know “network condition is bad”?
Increase/decrease rate?

## Slide 16: Adapting Output Rate
if network condition is bad
else if network condition is so-so
do nothing
else if network condition is good

## Slide 17: Adapting Output Rate
if network condition is bad
else if network condition is so-so
do nothing
else if network condition is good
Multiplicative
decrease
Additive
increase

## Slide 18: Question:
What should  and  be?

## Slide 19: Observation 1
Should never change your rate more than an equivalent TCP stream.

## Slide 20: Observation 2
 and  should depend on network conditions and current rate.
Notes: current rate high,

## Slide 21: Goal: Fair Share of Bottleneck
let r : current rate b : bottleneck bandwidth S : current share
Notes: current rate high,

## Slide 22: S vs 
1
S


## Slide 23: Value of 
(Assuming one receiver)

## Slide 24: Limit of 
M : packet size
 : round trip time
T : period between evaluation of 

## Slide 25: Limit of 
M : packet size
 : round trip time
T : period between evaluation of 

## Slide 26: Loss rate vs 

loss rate
1
1

## Slide 27: Value of m
where
is the loss rate
k is a constant
(Assuming one receiver)

## Slide 29: What is Needed?

## Slide 30: Estimating b : Packet Pair

## Slide 31: Estimating b : Packet Pair

## Slide 32: Estimating b : Packet Pair

## Slide 33: Evaluation

## Slide 34: More TCP-Friendly Rate Control

## Slide 35: TCP-Equation
Window size behavior in TCP/IP with constant loss probability
T. Ott, J. Kemperman, and M. Mathis
June 1997, HPCS 1997

## Slide 36: TCP-Equation
Equation-Based Congestion Control for Unicast Applications
Sally Floyd, Mark Handley, Jitendra Padhye, and Joerg Widmer. August 2000. SIGCOMM 2000

## Slide 37: Another Transport Protocol
Datagram Congestion Control Protocol (DCCP)
Implements congestion control but not reliability

## Slide 38: Rules
Transmission rate should match encoding rate
Transmission should not be too bursty

## Slide 39: Rate Control
Given a rate, how to encode the video with the given rate?

## Slide 40: Reduce Frame Rate
Live Video
Stored Video

## Slide 41: Reduce Frame Resolution
Live Video
Stored Video

## Slide 42: Increase Quantization
Live Video
Stored Video

## Slide 43: Drop AC components
Live Video
Stored Video

## Slide 44: Trouble with Stored Video
Reducing rate requires partial decoding and re-encoding
Solution: Layered Video

## Slide 45: Layered Video
or “Scalable Video”

## Slide 46: Layered Video
Layer 1
Layer 2
Layer 3
Notes: One of the better proposed solution is called RLM or receiver driven layered multicast. The idea is to divide a stream into multiple layers. The base layer encodes the video stream at a low bitrate, and each additional layer on top enhances its quality. The layers are sent onto different multicast channels, and receivers can choose the number of layers to receive based on their available bandwidth.

## Slide 47: Layering Scheme
Temporal (Frame Rate) Layering

## Slide 48: Layering Scheme
Spatial (Resolution) Layering

## Slide 49: Layering Scheme
DCT Layering; SNR (Quality) Layering
30
8
-6
-1
2
0
0
0
1
0
0
0
0
0
0
0
30
8
-6
-1
2
1
30

## Slide 50: Layering Scheme
Fine Granularity Scalability (FGS): e.g., MPEG-4
1 0 0 0 0 1 0 0
1 0 0 1 0 1 0 1
1 1 1 0 0 0 1 0
1 1 0 0 0 0 0 0

## Slide 51: Layered Video
SVC: Scalable Video Coding
  Base-layer plus enhancement layers
  Each received layer improves the quality
  Layer n+1 depends on layer n
MDC: Multiple Description Coding
  Layers are independent
  Each received layer improves the quality

## Slide 52: Layered Video
BUT: Layered video codecs are less bandwidth-efficient than single-layer codecs.

## Slide 53: Rate Adaptation
To increase rate, send more layers
To decrease rate, drop some layers

## Slide 54: MS Windows Streaming Media

## Slide 55: Intelligent Streaming
Multiple-Bit-Rate Encoding
Intelligent Bandwidth Control
  bit rate selection
  thinning
Intelligent Image Processing

## Slide 56: Intelligent Streaming
How exactly does it work?
Sorry, it’s proprietary

## Slide 57: Is WSM TCP friendly?
Measurements of the Congestion Responsiveness of Windows Streaming Media
J. Nichols et. al., NOSSDAV 2004
All figures taken from the original NOSSDAV presentation

## Slide 59: 340kbps clip, 725kbps bottleneck

## Slide 60: Transmission is Bursty

## Slide 61: 340kbps clip, 725kbps bottleneck

## Slide 62: 548kbps Clip - 725kbps Bottleneck

## Slide 63: 1128kbps Clip - 725kbps Bottleneck

## Slide 64: 725kbps Bottleneck
Buffering
Playout
Single Encoded Bit Rate

## Slide 65: 725kbps Bottleneck
Multiple Encoded Bit Rate
Buffering
Playout

## Slide 66: Conclusion
Two phases: buffering + playout
Not always TCP-friendly