## Slide 1: Streaming Protocol Suite
RTP, RTCP, RTSP

## Slide 2: Notes on HTTP Streaming (1)
On-Demand video streaming increasingly uses HTTP streaming
DASH: Dynamic Adaptive Streaming over HTTP
  ISO/IEC Standard:
    “Information technology — MPEG systems technologies — Part 6: Dynamic adaptive streaming over HTTP (DASH)”
    JTC 1/SC 29; FCD 23001-6

## Slide 3: Notes on HTTP Streaming (2)
DASH has a number of advantages
  Server is simple, i.e., regular web server
  No firewall problems (use port 80 for HTTP)
  Standard (image) web caching works
However, DASH does not
  Provide low latency for interactive, two-way applications (e.g., video conferencing)

## Slide 4: WebRTC (www.webrtc.org)
Web browsers with Real-Time Communications (RTC) capabilities via simple JavaScript APIs.
Pipeline for video conferencing in WebRTC (only one-way shown):
© Muaz Khan
RTP/RTCP

## Slide 5: Streaming Protocol Suite (1)
RTP: Real-Time Transport Protocol
RTCP: RTP Control Protocol
  Published in 1996 as RFC 1889, and superseded by RFC 3550 in 2003
  UDP, binary
  Transmission direction:
    RTP: from server to client (receiver)
    RTCP: either way (SR, RR)

## Slide 6: Streaming Protocol Suite (2)
RTSP: Real-Time Streaming Protocol
  Published as RFC 2326 in 1998
  TCP, text
  Transmission direction:
    Initiation from client, response by server
  “VCR”-type commands: PLAY, PAUSE, RECORD, TEARDOWN, …
  Session initiation: DESCRIBE, SETUP

## Slide 7: RTCP
Real-Time Transport Control Protocol

## Slide 8: RTCP
Real-Time Control Protocol
Provides
  receiver’s feedback
  network conditions
  time synchronization
  receiver’s description

## Slide 9: RTCP Packet Types
Sender’s Report (SR)
Receiver’s Report (RR)
Source Description (SDES)
Application Specific (APP)
BYE

## Slide 10: Fields in SR
NTP and RTP Timestamp
  relate media timestamp to real time
Sender’s stats
  byte count, packet count

## Slide 11: Fields in SR + RR
Reception Report
  Number of lost packets
  % of lost packets
  Inter-arrival jitter
  Timestamp of last SR
  Delay since last SR
tlsr
tdlsr
SR
RR

## Slide 12: Deducing Network Conditions
Packet Loss Rate
Interarrival Jitter
Round Trip Time

## Slide 13: Calculating Packet Loss Ratio (1)
For each source, keep
  first sequence number S0
  last sequence number Slast
Expected packets = Slast – S0 + 1
Count how many received packets

## Slide 14: Calculating Packet Loss Ratio (2)
Example:
  S0 = 53,466
  Slast = 1,349
  Expected packets Ce = Slast – S0 + 1 =
  Received packets Cr = 13,150
  Packet loss rate: 1 - Cr/Ce =

## Slide 15: Calculating Interarrival Jitter
Variance in packet spacing
Define:
  Pi.arrival_time
  Pi.media_timestamp
  Pi.transit_time

## Slide 16: Calculating Interarrival Jitter
Pi.transit_time =
  Pi.arrival_time - Pi.media_timestamp
Difference in transit time for two consecutive packets = D(i,i-1) =
  |Pi.transit_time – Pi-1.transit_time|

## Slide 17: Calculating Interarrival Jitter
Jitter after packet i = Ji (i.e., this is a continuously updated value)
Ji = (1-a) × Ji-1 + a × |D(i,i-1)| a: “weight” of most recent value vs. history
RFC 1889:
Ji = Ji-1 + ( |D(i,i-1)|  Ji-1)/16

## Slide 18: Calculating RTT (1)
tlsr
tdlsr
SR
RR
Calc RTT

## Slide 19: Calculating RTT (2)
RTT: 6.125 s – 5.250 s =
0.875 s

## Slide 20: Calculating ???
Pi.sender_byte_count
Pi.sender_packet_count

## Slide 21: RTCP Scaling (1)
RTCP session reports should scale from a few to thousands of participants
Constant rate control traffic: linear growth with the number of participants
Recommendation: limit RTCP traffic to 5% of bandwidth; limit RR to 1.25%
Vary report timing with random factor [0.5, 1.5] to calculated value t

## Slide 22: RTCP Scaling (2)
B: Fix RTCP bandwidth
N: Number of participants
S: Mean RTCP packet size
Sending interval =

## Slide 23: RTP
Real-Time Transport Protocol

## Slide 24: RTP Packet Format
RTP Header
RTP Payload
Header
RTP Payload

## Slide 25: RTP Header
9 bits: protocol version, alignment, header extension, CSRC length, marker

## Slide 26: RTP Header
Payload type: 7 bits
  Identify content
  E.g. 14: mp3; 32: MPEG-1

## Slide 27: RTP Header
Sequence number: 16 bits
  Packet sequence number

## Slide 28: RTP Header
Media timestamp: 32 bits
  The instant when the first byte in this packet was captured
  90 kHz timestamp (90,000 = 1 second)

## Slide 29: RTP Header
SSRC: 32 bits
  Random, unique in a session
  Identifies a source (not host!)

## Slide 30: RTP Header
Marker bit:
  Depends on payload
  E.g. beginning of frame

## Slide 31: On Receiving RTP packet
Check SSRC
  New source?
  Existing source? which one?
Check payload type
  Has format been changed?
  Which decoder should I use?

## Slide 32: RTSP
Real-Time Streaming Protocol

## Slide 33: RTSP (1)
Application-level protocol for establishing and controlling media sessions with real-time properties between end points control
Simple, text-based
Published in RFC 2326 (1998)
Uses TCP
Standard port: 554

## Slide 34: RTSP (2)
Allows VCR-type commands:
  DESCRIBE, SETUP, PLAY, TEARDOWN, PAUSE, RECORD, OPTIONS
On next slides:
  Black text – server command
  Blue text – client response

## Slide 35: RTSP Example
DESCRIBE rtsp://genesis/hackers.mov RTSP/1.0
RTSP/1.0 200 OK
Server: QTSS/v96
Cseq:
Content-Type: application/sdp
Content-Base: rtsp://genesis/hackers.mov/
Content-length: 179
v=0
s=hackers.mov
u=http://genesis.usc.edu/
e=admin@genesis.usc.edu
c=IN IP4 128.125.163.19
a=control:/
a=range:npt=0-3714.90167
m=audio 0 RTP/AVP 10
a=control:trackID=2

## Slide 36: RTSP Example
SETUP rtsp://genesis/hackers.mov
Transport: RTP/AVP;unicast;client_port=3000-3001
RTSP/1.0 200 OK
Server: QTSS/v96
Cseq:
Session: 4862038713701816342;timeout=6000
Transport: rtp/avp;server_port=2000-2001;client_port=3000-3001
PLAY rtsp://genesis/hackers.mov
Session: 4862038713701816342
RTSP/1.0 200 OK
Server: QTSS/v96
Cseq:
Session: 4862038713701816342
RTP-Info:url=hackers.mov;seq=59970;ssrc=477987946;rtptime=263102960

## Slide 37: RTSP Example
…
[Session plays]
…
TEARDOWN rtsp://genesis/hackers.mov
Session: 4862038713701816342
RTSP/1.0 200 OK
Server: QTSS/v96
Cseq:
Session: 4862038713701816342
Connection: Close

## Slide 38: SIP
Session Initiation Protocol

## Slide 39: SIP
Application-layer control (signaling) protocol for creating, modifying, and terminating sessions with one or more participants.
Text-based
RFC 3261
Has been accepted as a standard for VoIP (Note: Skype does not use SIP)

## Slide 40: Application-Level Framing
Expose details to applications
Let application decide what to do with a packet, not transport protocol

## Slide 41: MPEG + RTP
Application-Level Framing

## Slide 42: Previously, in CS5248
MPEG Compression
  Sequence, GOP, Picture, Slice, Macroblock, Block, DC/AC Coefficient
  I-Frame, P-Frame, B-Frame

## Slide 43: MPEG Frame Sizes
Constant Bitrate (CBR) vs. Variable Bitrate (VBR)

## Slide 44: Previously, on CS5248
RTP headers
  SSRC, Media Timestamp, Marker Bit, Payload Type ..
  Application-Level Framing

## Slide 45: You are Here
Network
Encoder
Sender
Middlebox
Receiver
Decoder

## Slide 46: Application-Level Framing

## Slide 47: How to send/recv?
Let the application decide, not the protocol stack.
Tennenhouse + Clark

## Slide 48: Application Knows Best
How to reorder packets
Whether to ignore loss
Which packet to retransmit

## Slide 49: Application Data Unit (ADU)
Can be processed individually, even out-of-order
Unit of error-recovery
  If part of an ADU is lost, the whole ADU is considered lost
8-Bit PCM audio: 1 ADU = 1 Byte
MPEG1 Video: 1 ADU =

## Slide 50: How to chop data into packets?
Every received packet should be useful (even in very lossy environments)
Ideally, 1 ADU in 1 packet

## Slide 51: RTP Payload Header
RTP Header
RTP Payload
Header
RTP Payload
MPEG Video-specific Header (32 bits)
MPEG-1? 2?
Temporal Reference
I? P? B?
Begin of Slice? End of Slice?
12 bytes
4-12 bytes
≤ Rest of IP packet

## Slide 52: RTP Header (Summary)
Ver: version, P: padding, X: extension, CC: CSRC count, M: marker, PT: payload type, sequence number, media timestamp, SSRC
4 bytes
4 bytes
4 bytes

## Slide 53: MPEG Video-specific Header
MBZ (5 bits)
  Unused. Must be 0.

## Slide 54: MPEG Video-specific Header
T (1 bit)
  1 if there is a MPEG-2 Extension Header after this header.

## Slide 55: MPEG Video-specific Header
Temporal Reference (10 bits)
  The ‘frame number’ of the current frame within the GOP.

## Slide 56: MPEG Video-specific Header
AN bit and N bit
  Set to 0 for MPEG-1.

## Slide 57: MPEG Video-specific Header
S (1 bit)
  Is there a sequence header in this packet?
  Repetition of sequence header is useful for resynchronization.

## Slide 58: MPEG Video-specific Header
BS (1 bit) and ES (1bit)
  BS is 1 iff the ‘first’ byte of this payload is a slice header.
  ES is 1 iff the last byte of this payload is the end of a slice.

## Slide 59: MPEG Video-specific Header
Picture Type (3 bits)
  I (1), P (2), B (3), D (4).

## Slide 60: MPEG Video-specific Header
Motion Vectors Information
  Get from most recent picture header.

## Slide 61: Fragmentation Rules
Sequence header: at the start of payload
GOP header: at the start of a payload (or follows Sequence header)
Picture header: at the start of a payload (or follows Sequence/GOP header)

## Slide 62: Fragmentation Rules
A slice must be either
  First data in the packet, or
  Follows integral number of slices
A slice may be fragmented if exceeds the size of a packet

## Slide 63: MP3 (MPEG-1, layer 3) Audio
MP3 audio can be encoded in two ways:
  RFC 2250
  RFC 3119
RFC 2250 describes the general MPEG-1 video/audio ADU framing
Problem: MP3 frames are not self-contained!

## Slide 64: MP3 Frame Structure
Each frame contains the header (Including the 4 byte MPEG header, optional 2 bytes CRC and 9, 17 or 32 bytes (depending on mono/stereo and MPEG 1 or 2) of side info
MP3 frames have a fixed length
Data of one ADU may span multiple frames
Problem: if one packet lost → multiple ADUs lost

## Slide 65: MP3 RFC 3119 Re-Arrangement
Idea: re-arrange data such that each packet is self-contained (i.e., decodable)
Effects:
  Better error resilience, but
  Variable length packets and
  Re-arrangement needs to be undone for decoder

## Slide 66: RFC 3119: Interleaving
Interleaving: interleave cycle of size 8
  Advantage: Consecutive packet losses have less effect
  Disadvantage: Send & receive latency is increased

## Slide 67: Other Thoughts
Packet losses on the Internet are often correlated, forming lost “packet trains”
What can be done to decorrelate losses?
How to measure audio and video quality?
  Objectively computed: PSNR (in dB)
  Subjective tests: MOS (range: 1 – bad to 5 – excellent)

## Slide 68: RFC 2250 versus RFC 3119
Frame-level loss simulation
  R: random loss
  G: Gilbert model
Note: Gilbert model produces correlated losses (“packet trains”)

## Slide 69: MP3 Sender/Receiver Structure
MP3 frames
Interleaved ADU frames
ADU frames
RTP packets
MP3 frames
Interleaved ADU frames
ADU frames
Server
Client
RTP packets
RFC 2250
RFC 3119

## Slide 70: Packet Size
1 MTU is 1500 bytes
IP Header size =
UDP Header size =
RTP Header size =
RTP Payload Header size =
Payload size =

## Slide 71: Network Tools
Iperf, Netstat, Tcpdump

## Slide 72: Network Tools
Iperf:
  Connection and throughput testing between two computers
Netstat:
  Information about ports and connections
Tcpdump:
  Packet trace information

## Slide 73: Iperf
On server:
  Iperf –s
On client:
  Iperf –c <host>
Default is TCP. Other options:
  –u: UDP; –b: bandwidth; –p: port#

## Slide 74: Port Numbers
RTSP: 554 (default)
RTP, RTCP: negotiated, e.g., 3000 and 3001
Note:
  Ports below 1024 on *nix require root (i.e., admin) privileges.
  Port numbers for different protocols can be found in file /etc/services.

## Slide 75: Iperf Example (TCP, Server)
Server:
$ ./iperf -s -p 8008 ------------------------------------------------------------ Server listening on TCP port 8008 TCP window size: 85.3 KByte (default) ------------------------------------------------------------ [ 4] local 137.132.81.189 port 8008 connected with 137.132.81.225 port 40455 [ 4] 0.0-10.0 sec 112 MBytes 94.0 Mbits/sec

## Slide 76: Iperf Example (TCP, Client)
Client:
$ ./iperf -p 8008 -c cervino.ddns.comp.nus.edu.sg ------------------------------------------------------------ Client connecting to cervino.ddns.comp.nus.edu.sg, TCP port 8008 TCP window size: 16.0 KByte (default) ------------------------------------------------------------ [ 3] local 137.132.81.225 port 40455 connected with 137.132.81.189 port 8008 [ ID] Interval Transfer Bandwidth [ 3] 0.0-10.0 sec 112 MBytes 94.3 Mbits/sec $

## Slide 77: Iperf Example (UDP, Server)
Server:
$ ./iperf -u -s -p 8008 ------------------------------------------------------------ Server listening on UDP port 8008 Receiving 1470 byte datagrams UDP buffer size: 108 KByte (default) ------------------------------------------------------------ [ 3] local 137.132.81.189 port 8008 connected with 137.132.81.225 port 46651 [ 3] 0.0-10.0 sec 1.25 MBytes 1.05 Mbits/sec 0.003 ms 0/ 893 (0%)

## Slide 78: Iperf Example (UDP, Client)
Client:
$ ./iperf -u -p 8008 -c cervino.ddns.comp.nus.edu.sg ------------------------------------------------------------ Client connecting to cervino.ddns.comp.nus.edu.sg, UDP port 8008 Sending 1470 byte datagrams UDP buffer size: 126 KByte (default) ------------------------------------------------------------ [ 3] local 137.132.81.225 port 46651 connected with 137.132.81.189 port 8008 [ ID] Interval Transfer Bandwidth [ 3] 0.0-10.0 sec 1.25 MBytes 1.05 Mbits/sec [ 3] Sent 893 datagrams [ 3] Server Report: [ ID] Interval Transfer Bandwidth Jitter Lost/Total Datagrams [ 3] 0.0-10.0 sec 1.25 MBytes 1.05 Mbits/sec 0.003 ms 0/ 893 (0%) $

## Slide 79: Netstat
$ netstat Active Internet connections (w/o servers) Proto Recv-Q Send-Q Local Address Foreign Address State tcp 0 0 cervino.ddns.comp.nus.e:ssh rogerz-d960.ddns.comp.:2200 ESTABLISHED Active UNIX domain sockets (w/o servers) Proto RefCnt Flags Type State I-Node Path unix 2 [ ] DGRAM 8356 @/var/run/hal/hotplug_socket unix 2 [ ] DGRAM 4241 @udevd unix 11 [ ] DGRAM 7384 /dev/log unix 2 [ ] DGRAM 22312596 unix 3 [ ] STREAM CONNECTED 22312457 unix 3 [ ] STREAM CONNECTED 22312456 unix 3 [ ] STREAM CONNECTED 22279908 unix 3 [ ] STREAM CONNECTED 22279907

## Slide 80: Netstat -l
Option -l: listening ports
$ netstat –l Active Internet connections (only servers) Proto Recv-Q Send-Q Local Address Foreign Address State tcp 0 0 localhost.localdomain:2208 *:* LISTEN tcp 0 0 *:mysql *:* LISTEN tcp 0 0 *:ssh *:* LISTEN tcp 0 0 localhost.localdomain:ipp *:* LISTEN tcp 0 0 localhost.localdomain:smtp *:* LISTEN tcp 0 0 *:862 *:* LISTEN tcp 0 0 *:http-alt *:* LISTEN tcp 0 0 *:8009 *:* LISTEN tcp 0 0 *:http *:* LISTEN tcp 0 0 *:webcache *:* LISTEN tcp 0 0 *:https *:* LISTEN

## Slide 81: Tcpdump
Needs ‘root’ privileges to run
Monitoring/capturing RTP traffic:
  $ tcpdump -T rtp -vvv src <host>