## Slide 1: Error Recovery

## Slide 2: Problems with Internet
Limited Bandwidth
Varying Conditions
Delay Jitter
Packet Loss
Delay
Heterogeneity
:

## Slide 3: You Are Here
Network
Encoder
Sender
Middlebox
Receiver
Decoder

## Slide 4: Overview
Characteristics of the Internet
General techniques
Error recovery for audio
Effect of loss on MPEG
Error recovery for MPEG

## Slide 5: Loss Characteristics of The Internet

## Slide 6: Characteristics of Internet
60-70% of paths do not show any loss
Those with loss have an average of 4.5 – 6% packet loss
[Paxson97] End-to-end Internet packet dynamics

## Slide 7: Packet Loss Pattern
1000
30
Number of
Occurrences
Burst
Length

## Slide 8: Packet Loss Pattern
1000
30
Number of
Occurrences
Burst
Length

## Slide 9: Characteristics of Internet
Bursts of loss are typically short (2-3 consecutively loss packets)
Long bursts do occur
Bursts may occur periodically

## Slide 10: Wireless Link
Loss rate measured in various environments (e.g., office) 10 ~ 20%
Up to 50% reported!

## Slide 11: Gilbert Model
GOOD
BAD
This model is used to simulate packet losses that may include packet trains.

## Slide 12: Gilbert Model
GOOD
BAD
p
q
1-q
1-p

## Slide 13: A Survey of Packet-Loss Recovery Techniques for Streaming Audio
Perkins, Hodson and Hardman
IEEE Network Magazine 1998

## Slide 14: Three Fundamental Techniques
Retransmission
Redundant data
Error concealment
Note: The optimal error recovery technique may be different for frame-based protocols (RTP) and chunk-based protocols (DASH).

## Slide 15: 1. Retransmission
1
2
3
4
1
2
4
3
3
X

## Slide 16: 2. Redundant Data
1
2
3
4
1
2
4
2
2
3
3
4
5
5
3

## Slide 17: 3. Error Concealment
2
4
1
2
3
4
1

## Slide 18: Retransmission
for audio

## Slide 19: Pros/Cons of Retransmissions
Pros
  Low bandwidth overhead
Cons
  Additional delay
  2-way channel needed with RTP (1-way channel with DASH)

## Slide 20: Scalable Retransmission
On packet loss
  T = random(0, RTT)
  wait for T
  multicast NACK
On receiving NACK from others
  suppress own NACK

## Slide 21: Retransmit when
Group size is small, or with DASH
Loss rate is low
Large latency acceptable

## Slide 22: Selective Retransmission
Retransmission based on priority of packets
Important/urgent packets are retransmitted first
Packets are only retransmitted when there is enough time [Papadopoulos and Parulkar, NOSSDAV 1996]

## Slide 23: Redundant Data
for audio

## Slide 24: Parity Forward Error Correction
1011001
1000010
0001001
XOR
0010010

## Slide 25: Parity Forward Error Correction
1011001
1000010
0001001
0010010

## Slide 26: Parity FEC Ordering

## Slide 27: Parity FEC Ordering

## Slide 28: Parity FEC Ordering

## Slide 29: Parity FEC Ordering

## Slide 30: Parity FEC Ordering

## Slide 31: Reed-Solomon Code
RS(n,k)
RS
n
k
(popular: n = 223)
(popular: k = 32)
Parity symbols
Data symbols

## Slide 32: Reed-Solomon Code
Data block (length n+k, e.g., 255)
Can correct up to 16 corrupted
symbols per block (32/2)

## Slide 33: Media Specific FEC
1
2
3
4
1
2
4
2
2
3
3
4
5
5
3
Transmit low quality chunk i+1 and high quality chunk i together.

## Slide 34: Pros/Cons of Redundant Data
Pros
  Small additional delay
  Only 1-way channel needed
Cons
  Computational complexity
  Limited correction ability
  Additional bandwidth overhead

## Slide 35: Interleaving

## Slide 36: Pros/Cons of Interleaving
Pros
  No bandwidth overhead
  “Several small errors vs. one large error”
Cons
  Additional delay

## Slide 37: Error Concealment

## Slide 38: Recreate Lost Information

## Slide 39: Effect of Loss on Audio
Speech
  Human ears can interpolate
  Loss up to length of phoneme can still be tolerable

## Slide 40: Insertion-based Repair
Splice
Silence Substitution
Noise Substitution
Repetition

## Slide 41: Other Repair Methods
Interpolation
Regeneration

## Slide 42: Error Concealment
More complex error concealment algorithms provide better performance (i.e., playback quality)

## Slide 43: Pros/Cons of Error Concealment
Pros
  No bandwidth overhead
  No (small) additional delay
Cons
  Computational complexity
  May result in visual artifacts
  May result in propagation errors

## Slide 44: Pros/Cons of Error Concealment
Note:
  Error concealment only works for very short amounts of time, i.e., 1 or 2 frames of video or a few milliseconds of audio. Larger interpolations will become very noticeable.
  Thus: Does not work for DASH (2 to 5 second streamlets).

## Slide 45: Colin’s Recommendations

## Slide 46: Non-Interactive Apps
Interleaving
FEC
Retransmission for unicast only

## Slide 47: Interactive Applications
Media Specific FEC

## Slide 48: Error Concealment
Repeat

## Slide 49: Packet Loss Effects on MPEG Video Sent over the Public Internet
Jill Boyce and Robert Gaglianello
ACM Multimedia 1998

## Slide 50: Measurement-based Study
Need to understand the problem before proposing solution

## Slide 51: Data Gathering Method
From: NYC13 , Austin21, London18
To: Holmdel, NJ

## Slide 52: Data Gathering Method
Video:
  Two 5-mins MPEG
  30 fps
  384 kbps and 1 Mbps
  GOP: IBBPBBPBBPBBPBB
  QSIF 176x112 and SIF 352x240
  One row per slice

## Slide 53: Average Packet Loss

## Slide 54: Frames Affected by Errors (1)
% Frames in Error
Packet Loss Rate

## Slide 55: Frames Affected by Errors (2)

## Slide 56: Overview of Error Recovery for Video

## Slide 57: Methods
Retransmission
Interleaving
Error Concealment
FEC
Limiting Error Propagation
  Reference Frame Selection

## Slide 58: Reference Frame Selection
I P B B P
X
I

## Slide 59: Methods
Retransmission
Interleaving
Error Concealment
FEC
Limiting Error Propagation
  Reference Frame Selection
  Changing Temporal Pattern

## Slide 60: Summary (1)
How to recover packet loss
  Retransmission
  FEC
  Error Concealment

## Slide 61: Summary (2)
How to limit the damage of errors
  Interleaving
  Key frame selection
  Change reference frame