## Slide 1: Error Recovery
Supplemental Slides

## Slide 2: Case Study: HD video conferencing
Korean Air, Inha University (Seoul), University of Southern California, Pratt & Whitney

## Slide 3
USC-Inha Two-way Experiments USC (Powell Hall of Engineering)
July 2005

## Slide 4
USC-Inha Two-way Experiments Inha University (Memorial Library)
July 2005

## Slide 5: KAL Network Infrastructure
Korean Air network infrastructure between Incheon, Kimpo, and Pusan
KAL network & external ISP (KT)
1 Gbps: ICN-GMP
50 Mbps: GMP-PUS
December 2005

## Slide 6: Network Measurements
End-to-end packet loss rates of the network path between Kimpo (GMP) and Incheon (ICN) observed during November 15-16, 2005
Network is shared with other business traffic
Loss rates are quite low
November 2005

## Slide 7: Hardware Preparation
3 computers purchased in Korea
Computers sent to USC with KAL
Software setup in the IMSC laboratories
  Linux installation
  RCS software installation
  Retransmission configuration
  End-to-end equipment test with local JVC cameras and displays
Computers sent back to KAL HQ
December 2005

## Slide 8: Hardware Test at KAL
Re-configuration for Sony HDR-HC1 cameras
December 2005
Local area network tests

## Slide 9: Experiments: ICN ◄▬► GMP
Asymmetric environment: 88 Mb/s & 50 Mb/s
Conclusion: ICN - GMP: sufficient BW for HD video
Sufficient headroom for data applications
December 2005
Bandwidth measurements
Visual quality
Required by RCS

## Slide 10: Experiments: ICN ◄▬► PUS
Asymmetric environment: 6 Mb/s & 1 Mb/s
GMP - PUS: initially insufficient BW for HD video
Investigated network routers with KAL IT help
Conclusion: replaced router to improve throughput; to be re-tested
December 2005
Bandwidth measurements
Visual quality

## Slide 11: Measurements: Packet Loss Rate
Path: ICN - PUS
Two packet sizes: 564 bytes and 940 bytes
Conclusion: GMP - PUS loss rate very high
December 2005
One-way packet loss rate
Two-way packet loss rate

## Slide 12: Packet Loss Error Recovery
Selective retransmission protocol is used to recover from lost data
Effectiveness of protocol is tested in lab environment
Gilbert Model is used to induce losses into transmission
Transmission delay is chosen to be 10 ms (expected latency in Korea)

## Slide 13: Packet Loss Error Recovery
Selective retransmission protocol
10% Loss Rate
5% Loss Rate
1% Loss Rate
With Retransmissions
With Retransmissions
With Retransmissions
Sept. - Dec. 2005
(ICN-GMP Link)

## Slide 14: Current Hardware Codecs
Hauppauge HD-PVR
Cavium PureVu™ CNW31XX

## Slide 15: HD-PVR H.264 Encoder

## Slide 17: Error Control Techniques for Interactive Low Bitrate Video Transmission over The Internet
Injong Rhee
SIGCOMM ‘98

## Slide 18: Basic Idea
“Better Late Than Never!”, or
Late packet is still useful

## Slide 19: MPEG Frame Pattern
I
B
B
P
B
B
P
I
P
B
B
P
B
B

## Slide 20: H.261 Error Propagation
I
P
P
P
P
P
P
X
X
X
X
X
X
I
P
P
P
P
P
P
X
X
X
X
retransmission
loss

## Slide 21: H.261 Frame Pattern
I
P
P
P
P
P
P
X
loss

## Slide 22: H.261 Frame Pattern
I
P
P
P
P
P
P
X
loss
X
X
retransmission

## Slide 23: PTDD
Periodic Temporal Dependency Distance
Large PTDD
  Higher Chance of Repair
  Longer Error Propagations
  Less Temporal Redundancy

## Slide 24: QAL
I
P
P
P
I
P
P
P
Base Layer
Enhancement
Layer

## Slide 25: QAL
I
P
P
P
I
P
P
P
Base Layer
+ FEC
Enhancement
Layer
X

## Slide 26: QAL + PTDD
I
P
P
P
I
P
P
P
Base Layer
Enhancement
Layer

## Slide 27: Error Propagation

## Slide 28: Recovery from Error Propagation

## Slide 29: Frame “quality”
PSNR =

## Slide 30: PSNR vs. Loss Rate
Packet Loss Rate
PSNR

## Slide 31: Today’s Summary

## Slide 32: How to recover packet loss
Retransmission
FEC
Error Concealment

## Slide 33: Limit the damage of error
Interleaving
Key frame selection
Change reference frame