## Slide 1: Cross-Sender Bit-Mixing Coding
Steffen Bondorf1, Binbin Chen2, Jonathan Scarlett3
Haifeng Yu3, Yuda Zhao4
1 NTNU Trondheim, Norway
2 Advanced Digital Sciences Center, Singapore
3 National University of Singapore
4 Advance.AI, Singapore
IPSN
2019-04-18
Notes: Authors are in alphabetical order

## Slide 2: Scenario: Multi-Sender, Multi-Receiver
E.g. in disaster recovery

## Slide 3: Why not use Scheduling?
There is a fundamental problem.
Assume the following setting for our scenario for each rescuer (receiver of data):
  Need to receive one d-byte packet from each neighboring sensor in receiving (RX) range
  Assume at most k neighboring sensors
  I.e., kd bytes of information need to be received by each rescuer
Can this be achieved in O(kd) airtime?
Not with scheduling [21]. It takes Ω(kd ln N) where N ≥ k is the amount of nodes.
  ln N stems from the problem that receivers’ best schedules are incompatible
Measure of interest R, the network utilization rate:
[21] M. Ghaffari, B. Haeupler, N. Lynch, and C. Newport. 2012. Bounds on Contention Management in Radio Networks. In International Symposium on Distributed Computing (DISC).

## Slide 4: The Idea: Allow for Collisions but Share the Damage
Divide the medium into Θ(kd) slots of common airtime → Cross-Sender
  Network utilization rate R = Θ(1)
Do not schedule entire packets, “schedule on the bit-level” → Bit-Mixing
Limit the amount of collisions per transmission in the network, such that every receiver can recover all the received data → Coding (BMC)
Senders
1
k
Θ(kd) slots
…...
Slot used by a sender that collides with slots used by other senders.
Slot used by a sender that do not collide with slots used by other senders.
Such a slot carries useful information.

## Slide 5: The Central Challenge in Bit-Mixing
All senders send simultaneously
Yet, the receiver must tell them apart
  A bit does not have a header to id its sender
  I.e., which slots are chosen by a sender?
We need a specifically constructed Low Collision Set (LCS) to achieve this
  An LCS consists of masking strings (>k)
  A masking string has “blank” bits and ”1” bits, a ”1” indicates a slot is chosen for transmission
  A masking string has a fixed weight (to transmit a fixed size data item)
  The LCS needs to be known by all, each node choses a masking string uniformly at random
BMC Phase 1:
Senders
1
k
Θ(kd) slots
…...
Senders send their chosen masking strings simultaneously and bit-aligned in Θ(kd) slots
Receiver receives a single message, the superimposition, and decodes the k masking strings with probability 1-δ

## Slide 6: Decoding the Masking Strings
Decisive property of the LCS: Chose any k masking strings, then each remaining string will collide with these in at most half of its slots with probability 1-δ
The superimposition of these k masking strings defines the message
Therefore, the message and the not chosen masking string only match in at most half of the slots
For decoding, simply iterate over all masking strings and compare
How to construct such an LCS?
Masking strings of the LCS
1
…...
|LCS|>k
Θ(kd) slots

## Slide 7: Background on Decoding: Non-Adaptive Group Testing (NAGT)
The BMC approach is reminiscent of Non-Adaptive Group Testing (NAGT)
  Can we reuse an existing design for our LCS?
NAGT literature provides
  R = Θ(1) (Θ(kd)) with exponential decoding complexity Ω(28d)
  polynomial decoding complexity but not R = Θ(1)
    R = O(1/k) for zero decoding error
    R = O(1/ln k) or R = O(1/f(δ)) for an error probability δ (f(δ)→∞ as δ→0)
  Maximum overlap of masking strings with the chosen k strings, then no fixed weight
BMC’s LCS:
  Network utilization rate R = Θ(1)
  Fixed weight of masking strings
  Simple construction of the LCS with high probability
  δ is tunable, the LCS will be of size Θ(k/δ)
  Polynomial decoding w.r.t. k, d, and δ
  Construction and proofs are in the paper and/or the technical report

## Slide 8: Data Transmission in a Second Phase
Encoding and decoding of data items:
  Remember the maximum overlap property of an LCS, it also holds among the k chosen ones
  Encode the data item with Reed-Solomon (RS) code with a rate of 1/2 to w RS symbols
  Send one RS symbol per slot defined in the masking string
  The receiver knows the used masking strings, therefore it knows their collisions
  Treat collisions as erased RS symbols (at most w/2) and ignore them
  The RS decoder can decode the assembled symbols into the original message
R = Θ(1), space and time complexity results for en-/decoding are in the paper
Senders send the bits in their encoded data items in slots specified by their respective masking strings
Receiver assembles the bits in slots specified by the masking strings and then decodes the data
slots
Senders send their chosen masking strings simultaneously
Receiver receives a single message, the superimposition, and decodes the k masking strings
First phase uses
slots

## Slide 9: Numerical Evaluation
t = 100,000 bytes of airtime available
Neighborhood size k = 100 and data size d = 25 to 100 bytes
  BMC requires 9kd = 22,500 to 90,000 bytes of airtime for sending
Measure: failure rate (fraction of data not delivered by the deadline)
  BMC δ = 10-4
Random Access packet scheduling: 1 divide t into t/d=l slots, send data with probability 1/k 2 a sender chooses exactly l/k slots in a uniformly random fashion
BMC competitors 1 as presented 2 repeatedly send as long as there is still airtime available

## Slide 10: A Look at the Physical Layer
Two challenges:
Bit alignment / synchronization
Modulation/demodulation of “blank”, “0” and “1” bits but there are only certain combinations of interest
Is it Feasible to Implement?
Senders send the bits in their encoded data items in slots specified by their respective masking strings
Receiver assembles the bits in slots specified by the masking strings and then decodes the data
Senders send their chosen masking strings simultaneously
Receiver receives a single message, the superimposition, and decodes the k masking strings
First Phase
All k senders send “blank”
or <k send a “1”, a “1” is received
We know the k masking strings
and only check for non-”blank” slots without collisions.
Demodulation into “0” or “1” bits
Combinations

## Slide 11: Using BMC in RFID Systems
Backscatter communication:
The RFID interrogator transmits a radio wave to the tags
Each tag reflects the radio wave or stays silent
Time synchronization for a single interrogator is given
  Multi-interrogator scenarios need synchronization between the interrogators
Modulation/demodulation of “blank”, “0” and “1” bits
  Radio wave reflected: “1” bit
  Tag stays silent: “blank” or “0” bit, depending on the BMC phase

## Slide 12: Using BMC with Zippy’s Physical Layer [45]
Zippy uses On-Off-Keying (OOK), BMC can be used without any modification to Zippy’s physical layer
  As before, “0” in the modulation is either “blank” or “0”, depending on the BMC phase
  At least one “1” sent in a slot, Zippy can demodulate the received signal to “1”
  Both BMC assumptions are satisfied
Zippy provides a distributed synchronization mechanism that suits BMC’s need for bit-alignment
  It achieves a synchronization error of tens of microseconds between any pair of neighbors
  Zippy sends at 1.36kbps, i.e., each bit takes about 700μs, multiple samples taken per bit
  Re-synchronization can be done every few seconds, takes only tens of milliseconds
[45] F. Sutton, B. Buchli, . Beutel, and L. Thiele. 2015. Zippy: On-Demand Network Flooding. In ACM SenSys.

## Slide 13: Using BMC in ZigBee Systems
Changes are required for more complex wireless systems
Synchronization mechanism required to achieve bit-alignment
  E.g., use Glossy [19] to achieve an error of <0.5µs. A ZigBee symbol takes 16µs tx time
  Periodic re-synchronization is required due to clock drift, every 0.1s should suffice
    Overhead is small, e.g., in a 3% in a network wit a diameter of 5 hops
Modulation/demodulation in BMC Phase 1
  ZigBee sends 4-bit symbols, therefore we propose to encode “1”-bit as “1111”-symbol
  We expect the receiver to sense the superimposition of “1111”-symbols from the energy level
Modulation/demodulation in BMC Phase 2
  Sender changes more often, demodulation baseline needs more frequent calibration
    One RS symbol in BMC is spread over two ZigBee symbols, add reference chips before
[19] F. Ferrari, M. Zimmerling, L. Thiele, and O. Saukh. 2011. Efficient network flooding and time synchronization
with Glossy. In IPSN.

## Slide 14: Summary and Conclusion
Scheduling packet transmissions in wireless multi-sender, multi-receiver networks leads to a fundamental medium utilization limit
We propose Cross-Sender Bit-Mixing Coding (BMC) to achieve R = Θ(1)
  BMC does not schedule packet transmissions
  BMC mixes the bits of different senders yet allows a receiver to decode the transmission
  We construct a low collision set (LCS) that can be used as a stand-alone NAGT matrix
    We prove several useful properties of the LCS (non-overlap, constant weight, decoding complecity)
    The paper provides a construction for an LCS
BMC has some demands on the physical layer
  Synchronization, modulation/demodulation of “blank”, “0” and “1” bits
that can be met by existing systems like RFID or ZigBee.
Thank you for your attention!